## Slide 1: Real Time Operating Systems & Real-Time Linux
Zonghua Gu

## Slide 2: What is a Real-Time System?
A real-time system is one in which the correctness of the system depends not only on the logical result of computation, but also on the time at which the results are generated
  J. Stankovic, 1988
Not necessarily “real-fast”!
  Predictability is the key
There was a man who drowned crossing a stream with an average depth of six inches
  J. Stankovic

## Slide 3: Hard or Soft?
Hard real-time systems cannot afford to miss any deadlines
  Engine control
  X-by-wire
  VxWorks, OSEKWorks, QNX
Soft real-time systems can afford occasional deadline misses
  In-vehicle multimedia
  Windows CE
Non-real-time systems
  Do they really exist?

## Slide 4: Embedded Systems
Systems with a small computer embedded within it
  The embedded computer forms the brain of the system
  Mechanical devices form the eyes (sensors) and muscles (actuators)

## Slide 5
Example RTE Systems
medical instruments
home appliances
office equipment
spacecraft
factory automation
military systems

## Slide 6: Categories of Embedded Systems
Stand-alone Embedded Systems
  Work in a stand-alone mode taking input and producing the desired output
Networked/Distributed Embedded Systems
  Embedded systems with network interface and accessible through the network.
Interacting set of embedded systems
  E.g., sensor networks, web camera based monitoring systems
Mobile Devices
  Mobile phones, PDAs

## Slide 7: Question
Are there real-time systems that are not embedded?
  Air traffic control systems
  Stock brokerage systems
Are there embedded systems that are not real-time?
  Almost all systems have some sort of soft real-time constraints
    Imagine your word processor taking 2 minutes to respond to you commands

## Slide 8: Characteristics of RTE Systems
Power Constraints
  Limited power source like a battery
  Minimize power demand by using less or low power hardware components
Cost
  Especially a constraint on mass produced consumer appliances like mobile phones, cars…
  Sometimes even a $0.10 decrease may lead to large savings
Reliability
  Should function for extremely long periods of time without developing faults
  Cannot reboot a car in motion, or a spacecraft in flight!

## Slide 9: Characteristics of RTE Systems
Performance
  Especially important in real-time systems
  Response within the deadline
Memory Size Limitations
  Important consideration while designing software
  Cannot have a 1GB Operating System!
  No hard disk!
Software Upgrade
  Software should be upgradable, cannot burn everything into ROM
  Remote uploading of software updates

## Slide 10: Characteristics of RTE Systems
Size
  A mobile phone the size of a brick will not be popular!
  Reducing size may impose additional limitations on power supply, heat dissipation
Limited User Interface
  May have very limited input/output interfaces
  Small keypad with few buttons for input
  Perhaps a two line LCD display
  Headless systems with no UI?
    Put a HTTP server on the machine and access it remotely?

## Slide 11: Challenges in RTE System Design
Limited OS support for programming
  Development has to be done on a separate development workstation
  Embedded OS is part of application code
    No user mode/kernel mode separation
Limited secondary storage
  Only limited non-volatile memory (ROM, Flash) available
  Cannot support virtual memory
Limited RAM
  Limitations on the code size
  Memory leaks can be fatal, eventually!

## Slide 12: Challenges in RTE System Design
Limited processing power
  Low speed (10-100 MHz) microprocessors
  Efficient code and simple algorithms required
Interaction with hardware
  Cannot completely hide the hardware complexity
  May have to directly interact with hardware
Absence of standard I/O devices
  Debugging may have to be done remotely

## Slide 13: What is Real Time ?
“ Real time in operating systems: The ability of the operating system to provide a required level of service in a bounded response time.”
- POSIX Standard 1003.1

## Slide 14: Real-Time in Handheld & Embedded Systems
Cost / Performance / Power / Weight Compromise
  Competitive, High-Volume, Low-margin Markets
  Maximum Feature-set, Add-ons, Responsive UI feel
  Device specs: minimal CPU & Memory & Battery Powered
  Real-time Requirements will never be alleviated by Improvements in Hardware Performance / Efficiency
Notes:     Software utilizing latest hardware technologies easily keep up with, and usually out-paces, advances in hardware technology
    If you don't believe that, go shopping (for a mobile phone)

## Slide 15: Soft Real-Time Systems
In a soft real-time system, it is considered undesirable, but not catastrophic, if deadlines are occasionally missed.
  Also known as “best-effort” systems
Examples:
  multimedia transmission and reception,
  networking, telecom (cellular) networks,
  web servers
  computer games.

## Slide 16: Hard Real-Time Systems
A hard real-time system has time-critical deadlines that must be met; otherwise a catastrophic system failure can occur.
  Requires formal verification/guarantees of being to always meet its hard deadlines
Examples:
  air traffic control
  vehicle control subsystems
  nuclear power plant control
Notes: Absolutely, positively, first time every time
(except for fatal errors).

## Slide 17: Components of an RTOS
Task (process or thread) management
  Scheduler
  Synchronization mechanism (semaphores, monitors)
Memory management
Interrupt service mechanism
I/O management
Development Environments
Communication subsystems
Board Support Packages (BSP)
Notes:     Interprocess communication (IPC)

## Slide 18: Real-Time Linux & PREEMPT_RT

## Slide 19: Outline
Real-Time Linux Background
  Real-Time Linux Evolution
  Real-Time Linux Enablers
Real-Time Inhibitors
  Interrupt Latency
  Kernel Locking
  Legacy Locking
Real-Time Kernel
  Interrupt Handlers, PI Mutex
  Performance / Benchmarks
  Acceptance
  Virtualization

## Slide 20: Linux in Real-Time Systems
UNIX systems (and Linux) are historically not Real-Time OS
UNIX-legacy Operating Systems were designed with operating principles focused on throughput and progress
  System resources must be shared fairly between users
  Fairness, progress and resource-sharing conflict with the requirements of time-critical applications
Notes: Not because of the Kernel’s Real-Time Performance!
  UNIX-legacy Operating Systems were designed with operating principles focused on throughput and progress
    User tasks should not stall under heavy load
    System resources must be shared fairly between users
  Fairness, progress and resource-sharing conflict with the requirements of time-critical applications
    VIP vs. General Admission
  User tasks should not stall under heavy load
Linux has lagged many commercial Unix's in Real-Time performance-enhancement and Real-Time capabilities

## Slide 21: Two Approaches
Dual-kernel approach
  Keep the regular Linux kernel intact
  Insert a small micro-kernel beneath regular Linux kernel
    Linux kernel handles non-real-time tasks/micro-kernel handles real-time tasks
  e.g. RT-Linux,. RTAI, Xenomai
Enhancing Linux kernel
  e.g. PREEMPT_RT patch, MontaVista Linux, TimeSys Linux,

## Slide 22: RT-Linux
Available as a patch to the regular Linux kernel
Provides an RT API for developers
Runs a Linux kernel as an idle thread (lowest priority) of the real-time kernel.
RT kernel and RT applications are kept as simple as possible and non-real-time applications (GUIs, file systems) are handled by standard Linux kernel.
Notes: Predictable delays.
  By its small size and limited operations.
Finer timer resolution.

## Slide 23: RTLinux ( Contd )
Real time threads and interrupt handlers never delayed by non-real-time threads
Micro-kernel:
  Very small and fast, this does not cause big delays.
  Supports EDF (Earliest Deadline First) and Fixed-Priority schedulers
Notes:   FIFO.
    Used to pass information between real-time process and ordinary Linux process.
    Designed to never block the real-time task.

## Slide 24: Linux vs RT-Linux

## Slide 25: RTAI (Real Time Application Interface)
A patch to the Linux kernel which introduces a hardware abstraction layer
Linux kernel is run as a background task running when no real time task is running.
  Linux application is able to execute without any modification
Notes: A broad variety of services which make realtime programmers' lifes easier
RTAI provides deterministic response to interrupts, POSIX compliant and native RTAI realtime tasks.
Hard real-time extension to the Linux kernel
Consists of:
  1 I/F to Linux HW Management (HAL): basically a data structure.
  3 basic components (dispatcher, scheduler, fifo's).
  1 I/F (set of functions) used in user tasks to initialize and start the components.
From a Linux point of view these entities populate modules.

## Slide 26: RTAI ( Contd )
Real time scheduler module
  Task functions
  Timing functions
  Semaphore functions
  Mailbox functions
  Intertask communication functions
Fifo services
Shared memory
Posix pthread and pqueue(msg queue)
Notes: RTAI is very much module oriented
RTAI provides better real-time support than RTLinux
  soft real-time in user space along with hard real-time in kernel space
  excellent performance in terms of low jitter and low latency
  better C++ support and more complete feature set
  availability of LXRT which allows user space applications in kernel space

## Slide 27: Real-Time and Linux Kernel Evolution
Gradual Kernel Optimizations over Time
  SMP Critical sections (Linux 2.x)
  Low-Latency Patches (Linux 2.2)
  Preemption Points / Kernel Tuning (Linux 2.2 / 2.4)
  Preemptible Kernel Patches (Linux 2.4)
  Fixed-time “O(1)” Scheduler (Linux 2.6)
  Voluntary Preemption (Linux 2.6)
Notes:   What Happened?
In 2003-04 Linux 2.6 RT Technology Regressed

## Slide 28: Real-Time Inhibitor: Critical Section Locking
Linux 2.6 Kernel Critical Sections are Non-Preemptible
  Critical sections protect shared resources, e.g. hardware registers, I/O ports, and data in RAM
  Critical sections must be locked and unlocked
  Locked critical sections are not preemptible
  Linux 2.6 Kernel has 11,000 critical sections
  Exhaustive Kernel testing to identify worst-case code paths
  Labor-intensive cleanup of critical sections
  Worst-case critical section length after cleanup still not acceptable
  No control over 3rd party drivers
Notes:   Critical sections are shared by Processes, Interrupts and CPUs.
  Effective protection is provided by the Spin-Lock Subsystem
  Maintenance, community education, policing / regression testing

## Slide 29: Real-Time Inhibitor: Interrupt Handlers
Linux 2.6 Kernel: Unbounded IRQ subsystem latencies
  Interrupts cannot be preempted
  Interrupts always have higher priority than application tasks
    Interrupt handlers always preempt application tasks unconditionally
    Task latency increases with hardware-interrupt load
Notes:   Unbounded SoftIRQ subsystem (“Bottom Half Processing”)
    Activated by HW IRQs (Timers, SCSI, Network)
    SoftIRQs re-activate, iterate
  Driver-level adaptations
    Network Driver NAPI adaption reduces D.o.S. effects of high packet loads

## Slide 30: Real-Time Inhibitor: Legacy Locking
Existing Locking Subsystems are not Priority-Aware
  System semaphore
    No support for priority inheritance
    No priority ordering of waiters
  Big Kernel Lock (BKL)
    Originally non-preemptible, now preemptible using system semaphore
      Can be released by blocking tasks, re-acquired upon wake-up
    No priority-awareness, or priority inheritance for contending tasks
  RCU (Read-Copy-Update) Locks in Network subsystem
    Read-optimized cached locking requiring race-free invalidation
  Read – Write Locks
    Classical blocking / starvation issues with no priority awareness

## Slide 31: Priority Inversion
Priority inversion:
  Tau1 is delayed by Tau2 for an unbounded amount of time

## Slide 34: The Fully Preemptible Linux Kernel
Dramatic Reduction in 2.6 Preemption Latencies
  Multiple Concurrent Tasks in Independent Critical Sections
  Generally Fully Preemptible  “No Delays”
    Non-preemptible: lowest-level interrupt management
    Non-preemptible: Scheduling and context switching code
Notes: Interrupt off paths and Optimization Flexibility
  RT Tasks designed to use Kernel-resources in managed ways can reduce or eliminate Priority-Inheritance delays
Adequate Instrumentation
  Latency timing, latency triggers & stack tracing, histograms
Design Flexibility
  Provides Full Access to Kernel Resources to RT Tasks
  Supports existing driver and application code
  User-space Real-Time

## Slide 35: Linux Real-Time Technology Overview
Linux 2.6 Kernel Real-Time Technology Enhancements
  Preemptible Interrupt Handlers in Thread Context
  Integrated Kernel Mutex with Priority Inheritance (PI)
    Preemptible PI Mutex protects Kernel Critical Sections
  PI Mutex Substituted for Non-Preemptible Kernel (SMP) Locks
    Big Kernel Lock (BKL) converted to PI Mutex
    Spin-Locks converted to PI Mutex
    Read-Write Locks converted to PI Mutex
    RCU Preemption Enhancements
  High Resolution Timers
Notes:   IRQ-Disable Virtualization for Drivers
    IRQ threads disabled without masking hardware
  User-Space Mutex
    Robustness / Dead-Owner / Priority Queuing

## Slide 36: Thread-Context Interrupt Handlers
Real-Time Solution: Interrupts in Thread Context
  Demote IRQ Handler Execution to Thread-based function
    IRQ Handlers scheduled in bounded-time by O(1) scheduler
    Inter-leaving of RT and IRQ tasks
    Real-Time tasks can have higher priority than IRQ handlers
Notes:   Incoming IRQ returns immediately
    IRQ activates corresponding Handler-thread (wake_up_process)
  RT IRQs operate in Vacated IRQ execution-space
    RT IRQs do not contend with common IRQs - Runs at IRQ Priority
    RT IRQ Latency Predictable
    Subject to Minimal Variation
  Promoted SoftIRQ Daemon Processes ALL Bottom-half activity
    SoftIRQs Preemptible
  Functionality of IRQ Handlers does not require IRQ context
    no special “IRQ Mode” Instructions
    IRQ Thread can have private stack
    Default: IRQs run in threads

## Slide 37: Thread-Context Interrupt Handlers
Threaded IRQs Pros
  RT IRQs do not contend with common IRQs
  IRQ Processing does not Interfere with task execution
  Flexible priority assignment
    can be arranged to emulate hardware-based priorities
  Interrupts run fully preemptible
Threaded IRQs Cons
  IRQ-Thread Overhead
    Scheduler must run to activate IRQ Threads
  IRQ Thread Latency
    IRQs no longer running at the highest priority
    Context-switch required to handle IRQ
    Response-Time / Throughput tradeoff

## Slide 38: Priority-Inheriting Kernel Mutex
New Synchronization Primitive
  Priority Inheritance
    Eliminate Priority Inversion delays
  Priority-ordered O(1) Wait queues
    Constant-time Waiter-list processing
    Minimize Task Wake-Up latencies
Notes:     Preemptible alternative to spin-locked / non-preemptible regions
    Expands on “Preemptible Kernel” Concept
    Spinlock typing preserved (maps spin_lock to RT or non-RT function )
  Enabler for User-space Real-Time Condition Variables & Mutexes Fundamental RT Technology
Preprocessor determines static function mapping
  Compile-time mapping, based on declared type
#define spin_lock(lock) PICK_OP(raw_spinlock_t, spin, _lock, lock)
PICK_OP #define PICK_OP(type, optype, op, lock) \ do { \ if (TYPE_EQUAL((lock), type)) _raw_##optype##op((type *)(lock)); \ else if (TYPE_EQUAL(lock, spinlock_t)) \ _spin##op((spinlock_t *)(lock)); \ else __bad_spinlock_type(); \ } while (0)
TYPE_EQUAL #define TYPE_EQUAL(lock, type) \ __builtin_types_compatible_p(typeof(lock), type *)
  Deadlock Detection
    Identify Lock-Ordering errors
    Reveal Locking cycles

## Slide 39: Real-Time Linux Kernel Evolution
SMP-Oriented Linux Kernel Optimizations
Kernel Critical sections Preemptible IRQ Subsystem Prioritized and Preemptible Mutex Locks with Priority Inheritance
High-Resolution Timers
“RT-Preempt” Kernel
Kernel Preemption outside Critical Sections, Preemptible “BKL”, O(1) Scheduler
Current Kernel 2.6
Kernel Preemption outside Critical Sections Spin-locked Critical Sections
“Preempt” Kernel 2.4
No preemption, Spin-locked Critical Sections
SMP Kernel 2.2 - 2.4
No Kernel preemption, “BKL” SMP Lock
SMP Kernel 2.x
No Kernel preemption
Early Kernel 1.x

## Slide 40: Kernel Evolution: Preemptible Code
Kernels
2.2-2.4
Preemptible
Kernel 2.4
Kernel 2.6
Preemptible
Non-Preemptible
Kernel 2.0
Real-Time
Kernel 2.6

## Slide 41: Real-Time Linux 2.6 Performance
Real-Time Linux 2.6 Kernel Performance
  Enables sub-millisecond control-loop response
  Enables Hard Real Time for qualified RT-aware Applications
SMP Kernel Performance
  Increased preemption in the Kernel also increases SMP throughput / efficiency
  SMP-safe code is by definition preemptible
  Any code that allows concurrent execution by multiple CPUs, also allows context switching and therefore preemption
Notes:   Far exceeds most stringent Audio performance requirements

## Slide 42: FRD
IRQ handler
Schedules
Thread 1
Thread 1 runs
Thread 1
Schedules
Thread 2
Thread 2 runs
etc
t
t
Fast Real-time Domain
Measurement tool

## Slide 43: Benchmarks
Target machine:
  Intel® Celeron® 800 MHz
Workload applied to the target system:
  Lmbench
  Netperf
  Hackbench
  Dbench
  Video Playback via MPlayer
CPU utilization during test:
  100% most of the time
Test Duration:
  20 hours

## Slide 44: Linux 2.6 Kernel – No Preemption
Line Chart Title
Source:

## Slide 45: Linux 2.6 Kernel – Real-Time Preemption
Line Chart Title
Source:

## Slide 46: Real-Time Response vs. Throughput
Efficiency and Responsiveness are Inversely Related
  Real-Time Preemption introduces overheads
    Mutex Operations more complex than spinlock operations
    Interrupt overhead
      Additional Task Switching
      Interrupt Preemption  Interrupt throughput reduction
Throughput
High responsiveness

## Slide 47: Real-Time and Linux Kernel Evolution
Today
  Real–Time Preemption
  High Resolution Timers
Future Innovation
  RT “awareness” extensions to Power-management subsystem
    Quick CPU Power+Freq Ramp for RT Tasks
    Power Level Scheduling Classes
  Virtualization / Hypervisor support for Real-Time
Notes:     Rate-Monotonic scheduling of RT tasks in independent VMs
    Per-VM QoS guarantees
  User-Space Robust Mutex

## Slide 48: Open Source
Ongoing Real-Time Development
  Patch against current Community Kernel (2.6.16)
  Maintained by Ingo Molnar from RedHat
  Architectures: i386, x86_64, PPC 32/64, Arm
Download from:
  http://www.kernel.org/pub/linux/kernel/projects/rt/
Notes:   Contributions from Community

## Slide 49: RT Synchronization on Multicore
Muticore processors introduce new issues and challenges to shared data synchronization.
Spinlocks are typically used to protect shared resource

## Slide 50: Deadlock on a Uni-Processor
A lower priority task holding a resource protected by SpinlockType A gets preempted by a higher priority task that later tries to acquire the same SpinlockType A
One solution: protect a TASK by wrapping the spinlock with a SuspendAllInterrupts () call so that the task cannot be preempted.

## Slide 51: Remote Blocking on Multicore
Remote blocking is defined as the duration for which a task waits for a shared resource to be released on a remote core.
Three tasks τ1, τ2, and τ3 in decreasing order of task priorities. Let tasks τ2 and τ3 be assigned to core P1, and task τ1, be assigned to core P2. Tasks τ1, and τ3 share a resource R protected by a SpinlockType S.
Left: τ3 acquires the resource R and gets preempted by task τ2 on core P1 before releasing R. In this case, task τ1 executing on core P2 might try to acquire the resource R and get blocked indirectly by τ2
Right: use of SuspendAllInterrupts () leads to a significant reduction in the remote blocking suffered by τ1 as

## Slide 52: Commercial RTOSes
LynxOS
QNX/Neutrino
VRTX
VxWorks
Notes: Commercial RTOSes different from traditional OS – gives more predictability
Used in the following areas such as:
  Embedded Systems or Industrial Control Systems
  Parallel and Distributed Systems
  Can be classified into Uniprocessor, Multiprocessor or Distributed Real-Time OS

## Slide 53: Lynx OS
Microkernel design
  Kernel footprint is small (28KB)
Small kernel provides essential services in scheduling, interrupt dispatching and synchronization
Memory protection through hardware MMUs
Self-hosted system
  development can be done in the same machine as target execution
Notes: Can function as a multipurpose UNIX OS

## Slide 54: Lynx OS: KPIs
Other services are provided by kernel lightweight service modules, called Kernel Plug-Ins (KPIs)
  New KPIs can be added to the microkernel and can be configured to support I/O, file systems, TCP/IP, streams and sockets
KPIs are multi-threaded, which means each KPI can create as many threads as it want
Inter-KPI communication incurs minimal overhead, consuming only very few instructions
Notes: There is no context switch when sending a message to a KPI
  For example, when a RFS (Request for Service) message is sent to a File System KPI, this does not request a context switch
  Hence run-time overhead is minimum
  Further, inter

## Slide 55: Lynx OS Interrupt Handling
Each device driver has an interrupt handler and kernel thread
  The interrupt handler carries the first step of interrupt handling; If it does not complete the processing, it sets an asynchronous trap to the kernel
  Later, when kernel can respond to the software interrupt, it schedules an instance of the kernel thread to complete the interrupt processing
Notes: Applications make I/O requests to I/O system through system calls
Kernel directs I/O request to the device driver

## Slide 56: QNX/ Neutrino
POSIX-compliant Unix-like real-time operating system.
Microkernel design – kernel provides essential threads and real-time services
use of a microkernel allows users (developers) to turn off any functionality they do not require without having to change the OS itself.
The kernel is quite small (footprint is 12kb).
Notes: fitting in a minimal fashion on a single floppy, and is considered to be both very fast and fairly "complete."

## Slide 57: QNX/ Neutrino (contd..)
Typical Microkernel:
  Every driver, application, protocol stack, and file system runs outside the kernel, in the safety of memory-protected user space.
  As a result, virtually any component can fail - and be automatically restarted -without affecting other components or the kernel.
Maximize application portability with extensive support for the POSIX standard, which lets you quickly migrate Linux, Unix, and other open source programs

## Slide 58: QNX/ Neutrino (contd..)
QNX is a message passing operating system
  Messages are basic means of IPC among threads
  Follows a message based priority tracking feature
    Msg receiver priority is determined by msg sender priority

## Slide 59: VxWorks
From Wind River (part of Intel)
The core attributes: high performance, reliability, determinism, low latency and scalability.
Real-Time Embedded Application
Graphics
Multiprocessing
Internet
Java Support
POSIX Library
File System
WindNet Networking
Wind Microkernel
Core OS:
Notes: Current Version: VxWorks 6.0 
VxWorks is the most established and most widely deployed device software operating system.
Currently more than 300 million devices running VxWorks enabled.

## Slide 60: VxWorks (contd..)
MMU-based memory protection
Extensive POSIX 1003.1, .1b, .1c compatibility (including pthreads )
To reduce context-switch time
  Saves only those register windows that are actually in use
  When a task’s context is restored, only the relevant register window is restored
  To increase responsiveness, it saves the register windows in a register cache – useful for recurring tasks
Notes: (on a Sparc) Scheduling
  Uses preemptive priority with round robin scheduling to accommodate for both real-time and non-real-time tasks

## Slide 61: VxWorks (contd..)
Distinguishing features
  efficient POSIX-compliant memory management
  multiprocessor facilities
  shell for user interface
  symbolic and source level debugging capabilities
  performance monitoring
Used in the Mars Exploration Rovers Spirit and Opportunity and the Mars Reconnaissance Orbiter

## Slide 62: Open-Source RTOSes
eCos
Free RTOS
MicroC/OS

## Slide 63: eCos ( Embedded Configurable OS )
Highly Configurable RTOS
  Application-specific
  Multiple implementation of kernel functions including scheduling, allocating memory and interrupt handling
Easily Portable
  Hardware Abstraction Language (HAL)
Notes: Native API, POSIX API, µITRON API, C API

## Slide 64: eCos ( Contd …)
eCos is targeted at high-volume applications in consumer electronics, telecommunications, automotive, and other deeply embedded applications.
No kernel/user mode separation
  Less protection, better efficiency
Implemented using C++
GNU debugger (GDB) support

## Slide 65: eCos ( Contd …)
Features
  Choice of scheduling algorithms
  Choice of memory-allocation strategies
  Timers and counters
  Exception handling
  ISO C library, Math library
  Rich set of synchronization primitives
Notes:   Support for interrupts and DSRs
  Host debug and communications support

## Slide 66: eCos ( Contd …)
http://www.cotsjournalonline.com/home/article.php?id=100164

## Slide 67: FreeRTOS
Simple , Portable , Royalty free , Concise
Cross development from a standard Windows host
Choices of different scheduling policies
  Pre-emptive: Always runs the highest available task. Tasks of identical priority share CPU time (fully pre-emptive with round robin time slicing).
  Cooperative: Context switches only occur if a task blocks, or explicitly calls taskYIELD().
Notes: Mini Realtime Kernel
Message Queue

## Slide 68: FreeRTOS ( Contd )
Supports 8, 16 and 32bit microcontrollers including ARM7, AVR, 8051, MSP430 and x86.
  Ports are available for the Philips ARM7, TI MSP430, Renesas (Hitachi) H8/S, Atmel AVR, Motorola/Freescale HCS12, Motorola/Freescale ColdFire, and others.
A smaller and easier real-time processing alternative for applications where larger RTOSes won't fit, like eCos and embedded Linux (or Real Time Linux).
Notes: Majority of source code common to all supported development tools
RTOS kernel uses multiple priority lists

## Slide 69: MicroC/OS
Highly portable, ROMable, very scalable, preemptive real-time, multitasking kernel
Has ports for most popular processors and boards in the market
Suitable for use in safety critical embedded systems such as aviation, medical systems and nuclear installations
  Approved for use in DO-178B aerospace systems
Notes: MicroC/OS has been designed as a small footprint real time pre-emptive OS that was designed for embedded use on 8 bit platforms upwardsOver 100 microprocessors are supported
Also known as µC/OS II or uC/OSII

## Slide 70: MicroC/OS ( Contd )
kernel is preemptive real time, managing up to 64 tasks, with up to 56 tasks for application tasks
Each task has a unique priority and its own stack
  Round robin scheduling between same-priority tasks is not supported
Memory management is performed using fixed size partitions.
Notes: µC/OS II features
  reentrant functions and is portable to different processors
operating system uses semaphores to restrict access to resources shared by multiple elements of the system

## Slide 71: MicroC/OS ( Contd )
Each thread (task) is an infinite loop and can be in any one of the following 5 states
  Dormant, Ready, Running, Waiting, ISR
IPC services include mailboxes, queues, and semaphores
Notes: µC/OS II is a multitasking operating system

## Slide 72: Other RTOS
* Opensource * Commercial
* Nut/OS * BeOS * µnOS
* TRON Project * ChorusOS * RMX
* MicroC/OS-II * RSX-11
* OS-9 * RT-11
* OSEKtime * RTOS-UH
* pSOS * VRTX