## Slide 1: MP Real-Time Scheduling

## Slide 2: As Moore’s law goes on…
Number of transistor/chip doubles every 18 to 24 mm
Notes: the number of transistors that can be inexpensively placed on an integrated circuit is increasing exponentially, doubling approximately every two years
Patterson & Hennessy: number of cores will double every 18 months, while power, clock frequency and costs will remain constant

## Slide 3: …heating becomes a problem
P  V  f: Clock speed limited to less than 4 GHz
4004
8008
8080
8085
8086
286
386
486
Pentium
P1
P2
P4
Pentium Tejas
cancelled!
P3
Hot-plate
Nuclear
Reactor
STOP
Year
Power (W)

## Slide 4: Keeping Moore’s law alive
Exploit the immense number of transistors in other ways
Reduce gate sizes while keeping CPU frequency relatively low
Use a higher number of slower logic gates
In other words:
Switch to Multicore processor!

## Slide 5: Solution
Denser chips with transistor operating at lower frequencies
MULTICORE SYSTEMS
Use a higher number of slower logic gates

## Slide 6: Multicore Motivations
1. Standard processor over-clocked 20% 2. Standard processor 3. Two standard processors each under-clocked 20%
Notes: Two or more processor cores on the same chip
  Intel Core Duo processor
Semiconductor trends
  More transistors available per die
  Clock scaling reaching limits due to power constraints. An empirical study suggests that a 1% clock increase results in a 3% power increase.
    Moore’s Law has hit a wall due to power constraints

## Slide 7: The Multicore invasion
Intel’s Core2, Itanium, Xeon: 2, 4 cores
AMD’s Opteron, Athlon 64 X2, Phenom: 2, 4 cores
IBM-Toshiba-Sony Cell processor: 8 cores (PSX3)
Microsoft’s Xenon: 3 cores (Xbox 360)
ARM’s MPCore: 4 cores
Sun’s Niagara UltraSPARC: 8 cores
Tilera’s TILE64: 64-core
Nios II: x soft Cores
TI, Freescale, Atmel, Broadcom,Picochip (picoArray up to 300 DSP cores), ...
Notes: Network Processors andare being replaced by multicore chips (Broadcom)
DSP
Picochip: communication domain

## Slide 8: Task Model
Independent periodic taskset with n tasks
For each task ti
  Ci: Worst-Case Execution Time
  Di: Relative deadline
  Ti: Period
Each task consists of an infinite sequence of jobs
  The kth job of task ti is denoted jik

## Slide 9: Multiprocessor models
identical multiprocessors:
  each processor has the same computing capacity
uniform multiprocessors:
  different processors have different computing capacities
heterogeneous multiprocessors:
  each (task, processor) pair may have a different computing capacity

## Slide 10: Identical vs heterogenous cores
ARM’s MPCore
IBM Cell Processor
4 identical ARMv6 cores
One Power Processor Element (PPE)
8 Synergistic Processing Element (SPE)

## Slide 11: Multiprocessor Models
Identical multiprocessors: each processor has the same speed
P1
P2
P3
Task T1
Task T2
background – problem – results

## Slide 12: Multiprocessor Models
Uniform multiprocessors: different processors have different speeds
P1
P2
P3
Task T1
Task T2
x
x/2
x/3
y
y/2
y/3
background – problem – results
speed = 1
speed = 2
speed = 3

## Slide 13: Multiprocessor Models
background – problem – results
Heterogeneous multiprocessors: each (task, processor) pair may have a different relative speed, due to specialized processor architectures
x/2
x/3
x
CPU
DSP chip
Graphics co-processor
Graphics-intensive task:
Number-crunching task:
x/2
x/3
y
1.5 y
y
Task T1
Task T2

## Slide 14: MP Scheduling
Many NP-hard problems
  Few optimal results
  Heuristic approaches
Only sufficient schedulability tests
Active research topic

## Slide 15: Global vs partitioned scheduling
Global scheduling
  All ready jobs are kept in a common (global) queue; when selected for execution, a job can be dispatched to an arbitrary processor, even after being preempted
Partitioned scheduling
  Each task may only execute on a specific processor
CPU1
CPU2
CPU3
t1
t2
t3
t2
t1
t3
t4
t5
CPU1
CPU2
CPU3
t1
t2
t3
t1
t4
t5
t2
Global scheduling:
Single system-wide queue
Partitioned scheduling:
per-processor queues
Notes:   A task may execute on any processor
  A preempted job may resume on any processor
All ready tasks are kept in a common (global) queue
When selected for execution, a task can be dispatched to an arbitrary processor, even after being preempted
Single system-wide queue or multiple per-processor queues:

## Slide 16: Global Scheduling
Advantages:
  Supports load-balancing
    More effective utilization of processors
    Unused processor time can easily be reclaimed
  More effective slack reclaiming and overload management
  Supported by most multiprocessor operating systems
    Windows, Linux, MacOS...
Disadvantages:
  Migration cost: can be mitigated by proper HW (e.g., MPCore’s Direct Data Intervention)
  Few schedulability tests  Active research topic
Notes:   Easier re-scheduling (dynamic loads, selective shutdown, etc.)
  Number of preemptions
  Weak theoretical framework
  • Poor resource utilization for hard timing constraints
    – No more than 50% resource utilization can be guaranteed
  • Suffers from several scheduling anomalies
    – Sensitive to period adjustments
    Lower average response time

## Slide 17: Partitioned scheduling
Advantages:
  Mature scheduling framework
  Uniprocessor scheduling theory scheduling are applicable
  Uniprocessor resource access protocols (PIP, PCP…) can be used
Partitioning of tasks can be automated
  e.g., with bin-packing algorithm
Disadvantages:
  No load-balancing
  Surplus CPU time cannot be shared among processors
Notes: cannot exploit all unused execution time

## Slide 18: Partitioned Scheduling
The scheduling problem reduces to:
Bin-packing
problem
Uniprocessor
scheduling
problem
+
NP-hard
Various heuristics algorithms
First Fit (FF)
Best Fit (BF)
Worst Fit (WF)
Next Fit (NF)
Well known
EDF
Utot ≤ 1
t2
t1
t3
t4
t5
RM
(RTA)
...
Notes: FF, NF, BF, FFDU, BFDD, etc.
in the
strong sense
Global (work-conserving) and partitioned approaches are incomparable
Two steps:
  1. Determine a mapping of tasks to processors
  2. Perform run-time scheduling
The Earliest Deadline First (EDF) scheduling algorithm
  - provably optimal (utilization bound = 1.0) on uniprocessors
Partitioned with EDF 
  Assign tasks to the processors, such that no processor’s capacity is exceeded
  Schedule each processor using EDF

## Slide 19: Partitioned Scheduling
Bin-packing algorithms:
  – The problem concerns packing objects of varying sizes in boxes (”bins”) with the objective of minimizing number of used boxes.
Application to multiprocessor systems:
  – Bins are represented by processors and objects by tasks.
  – The decision whether a processor is ”full” or not is derived from a utilization-based feasibility test.
Assumptions:
  – Independent, periodic tasks
  – Preemptive, uniprocessor scheduling (RM)

## Slide 20: Partitioned scheduling
Complexity of schedulability analysis for partitioned scheduling: (Leung & Whitehead, 1982)
  The problem of deciding whether a task set is schedulable on m processors with respect to partitioned scheduling is NP-complete
Consequence:
  There cannot be any pseudo-polynomial time algorithm for finding an optimal partition of a set of tasks unless P = NP.

## Slide 21: Example: RMFF
Rate-Monotonic-First-Fit (RMFF): (Dhall and Liu, 1978)
  Let the processors be indexed as 1, 2, …
  Assign the tasks in the order of increasing periods (that is, RM order).
  For each task Ti, choose the lowest previously-used processor j such that Ti, together with all tasks that have already been assigned to processor j, can be feasibly scheduled according to the utilization-based RM-feasibility test.
  Additional processors are added if needed.

## Slide 22: Our Assumptions for Global Scheduling
Identical multiprocessors
Work-conserving:
  At each instant, the highest-priority jobs that are eligible to execute are selected for execution upon the available processors.
  a processor is never left idle while an active job exists (unless migration constraints prevent the task from executing on the idle processor
Notes: Task execution is assumed to be ”greedy”:
  If higher-priority tasks occupy all processors, a lower-priority task cannot grab a processor until the execution of a higher priority task is complete.
Task execution is assumed to be ”greedy”:
  If higher-priority tasks occupy all processors, a lower-priority task cannot grab a processor until the execution of a higher priority task is complete.

## Slide 23: Additional Assumptions
Independent tasks
Preemption and Migration support
  For global schedulers, a preempted task can resume its execution on a different processor with 0 overhead
  Cost of preemption/migration integrated into task WCET
No job-level parallelism
  the same job cannot be simultaneously executed on more than one processor
Notes: The independence assumtion can be later removed, considering blocking times and shared resource protocols.

## Slide 24: Source of Difficulty
The “no job-level parallelism” assumption leads to difficult scheduling problems
“The simple fact that a task can use only one processor even when several processors are free at the same time adds a surprising amount of difficulty to the scheduling of multiple processors” [Liu’69]
CPU1
CPU2
CPU3
Notes: The ”root of all evil” in global scheduling: (Liu, 1969)
  Few of the results obtained for a single processor generalize directly to the multiple processor case; bringing in additional processors adds a new dimension to the scheduling problem. The simple fact that a task can use only one processor even when several processors are free at the same time adds a surprising amount of difficulty to the scheduling of multiple processors.

## Slide 25: Global scheduling example
CPU1
CPU2
CPU3
Global queue
(ordered according to a given policy)
t1
t2
t3
The first m tasks are scheduled upon the m CPUs
t2
t1
t3
t4
t5
Notes: There is a global queue in which ready tasks ready are placed, according to a certain policy. When there is a free CPU the first task is removed from the queue and is scheduled. When a new task arrives with priority higher than one of the executing tasks, it preempts the executing task with lowest priority. If a task on a different CPU finishes its execution, the preempted task can “migrate” to the free CPU and continue its execution.

## Slide 26
t3
CPU1
CPU2
CPU3
t1
t2
When a task finishes its execution, the next one in the queue is scheduled on the available CPU
t2
t1
t3
t4
t5
t2
t1
t3
t4
t5
t4
Global queue
(ordered according to a given policy)
Global scheduling example

## Slide 27
CPU1
CPU2
CPU3
t1
t2
When a higher priority task arrives, it preempts the task with lowest priority among the executing ones
t2
t1
t3
t4
t5
t4
t3
t2
t1
t3
t4
t5
t3
t3
Global queue
(ordered according to a given policy)
Global scheduling example

## Slide 28
CPU1
CPU2
CPU3
t1
t2
When another task ends its execution, the preempted task can resume its execution
t2
t1
t3
t4
t5
t4
t3
t3
t4
t3
t4
t2
t5
t3
t4
Task t4 “migrated” from
CPU3 to CPU1
Global queue
(ordered according to a given policy)
Global scheduling example

## Slide 29: Global scheduling
The m highest priority ready jobs are always executing
Work-conserving scheduler
  No processor is ever idle when the ready queue is non-empty
CPU1
CPU2
CPU3
t1
t2
t3
t2
t1
t3
t4
t5

## Slide 30: Global vs. Partitioned
Global (work-conserving) and partitioned scheduling algorithms are incomparable:
  There are tasksets that are schedulable with a global scheduler, but not with a partitioned scheduler, and vice versa.

## Slide 31: Global vs Partitioned (FP)
A taskset schedulable with global scheduling, but not partitioned scheduling
  t1 =(1,2); t2 =(2,3); t3 =(2,3)
  Global FP scheduling w/ priority assignment p1>p2>p3
One possible execution trace (another legal trace is for T1 to always stay on Processor 1):
Also feasible for priority assignment p2>p1>p3

## Slide 32: Global vs Partitioned (FP)
A taskset schedulable with partitioned scheduling, but not global scheduling
Example: t1=(4,6); t2=(7,12); t3=(4,12); t4=(10,24), t1 and t3 are assigned to Processor 1; t2 and t4 are assigned to Processor 2
Execution trace w/ partitioned FP scheduling w/ RM priority assignment (p1>p2>p3>p4)

## Slide 33: Global vs Partitioned (FP)
Global FP scheduling w/ priority assignment p1>p2>p3>p4:
t1=(4,6); t2=(7,12); t3=(4,12); t4=(10,24)

## Slide 34: Difficulties of Global Scheduling
Dhall’s effect:
  With RM, DM and EDF, some low-utilization task sets can be unschedulable regardless of how many processors are used.
Dependence on relative priority ordering:
  Changing the relative priority ordering among higher-priority tasks may affect schedulability for a lower-priority task.
Hard-to-find critical instant:
  A critical instant does not always occur when a task arrives at the same time as all its higher-priority tasks.
Scheduling anomalies
  Decreasing task execution time or increasing task period may cause deadline misses
Notes: A critical instant does not always occur when a task arrives at the same time as all its higher-priority tasks.

## Slide 35: Dhall’s effect
T
Example: m processors, n=m+1 tasks, Di = Ti
t1 ,…, tm = (1,T-1) tm+1 = (T,T)
Global RM/DM/EDF can fail at very low utilization
One solution: assign higher priority to tasks with
higher utilization
DEADLINE
MISS
m light tasks
1 heavy task
Utot1
Notes: Observation: RM, DM and EDF only account for task periods!
  Execution times are not considered.
Solution: Dhall’s effect can be avoided by assigning higher priority to tasks with higher utilization

## Slide 36: Priority Assignment
Impact of relative priority ordering:
  Response time of a task depends on the relative priority ordering of higher-priority tasks
    Not true for a uniprocessor system
  This means that well-known uniprocessor methods for finding optimal priority assignments (e.g., Audsley, 1991) cannot be applied
Consequence:
  New methods for constructing optimal multiprocessor priority assignments are needed!

## Slide 37: Priority Assignment

## Slide 38: Priority Assignment

## Slide 39: Priority Assignment

## Slide 40: Feasibility Test

## Slide 41: Avoiding Dhall’s effect

## Slide 42: Hard-to-find critical instant
A critical instant does not always occur when a task arrives at the same time as all its higher-priority tasks.
  Finding the critical instant is a difficult problem
  Recall that knowledge about the critical instant is a fundamental property in uniprocessor feasibility tests.
Consequence:
  New methods for constructing effective multiprocessor feasibility tests are needed

## Slide 43: Critical-Instant Example

## Slide 44: MP Scheduling Anomalies
Decrease in processor demand (decreasing task execution time or increasing task period) may cause deadline misses!
Anomaly 1
  Decrease in processor demand from higher-priority tasks can increase the interference on a lower-priority task because of change in the time when the tasks execute
Anomaly 2
  Decrease in processor demand of a task negatively affects the task itself because change in the task arrival times cause it to suffer more interference
Notes: EDF does not suffer from execution-time anomalies, but does suffer from period anomalies.

## Slide 45: Anomaly 1

## Slide 46: Anomaly 1

## Slide 47: Anomaly 2

## Slide 48: Anomaly 2
Another example where the critical instant for task c does not occur at time 0 when it arrives at the same time as all its higher-priority tasks.
c
20
b
a
c
23
C’s deadline
missed here

## Slide 49
PFair Scheduling

## Slide 50: PFair Scheduling Properties
  Pfair algorithms are optimal for (periodic and sporadic) systems with implicit deadlines (deadline = period) on uni- and multiprocessor
  Pfairness satisfied ⇒ deadlines are met for the periodic scheduling problem
Real-time scheduling algorithms based on proportionate fairness offers:
  low output jitter
  peaceful coexistence of real-time and non-real-time tasks
Notes: Goal: schedule on a multiprocessor a set of periodically arriving hard real-time tasks with constant execution time in order to meet deadlines
  ”fairness for free”

## Slide 51: Pfair Scheduling
Based on GPS (Generalized Processor Sharing), with a lag bounded by one
  In any interval t, a task with utilization U will execute for an amount W, with Ut-1 < W < Ut+1
Different Pfair algorithms (PF, PD, PD2) [Anderson et al.]
  All these algorithms incur large number of preemptions/migrations
Notes: Other optimal algorithms: LLREF, EKG, BF

## Slide 52: Task Model

## Slide 53: Task Model

## Slide 54: Proportional Progress

## Slide 55: Question
Is there a schedule that only context-switches tasks at integer boundaries?

## Slide 56: Proportional Progress

## Slide 57
Allocation error with respect to the ideal system
  lag(T, t, S) = ideal(T, t) – actual(T, t, S)
Positive  behind, negative  ahead, zero  punctual
allocation error
for task T at
time t
total allocation
to T in the ideal
schedule over [0,t)
total allocation to T in the
schedule under
consideration over [0,t)

## Slide 58
Example: Task T with wt(T) = 3/8
3/8
1
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
0
1
2
-1
-2
Ideal
Allocation
Possible
allocations
to a periodic
task
Lag

## Slide 59
3/8
1
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
0
1
2
-1
-2
Ideal
Allocation
Possible
allocations
to a periodic
task
Lag
A schedule is Pfair iff
(T, t :: 1 < lag(T, t) < 1)

## Slide 60: Lag of a Periodic Task
Lag(T,u) = ideal share of T in [0,u) – Pfair(T,u).
  lag(T, u) < 0  T is over-allocated at time u.
  lag(T, u) > 0  T is under-allocated at time u.
0 1 2 3 4 5 6 7 8 9 10 11
6
5
4
3
2
1
0
total share of task with weight 3/5.
time
ideal
Pfair
Under-allocated
Over-allocated

## Slide 61: proportionate progress

## Slide 62: How far from zero can the lag be?

## Slide 63: PFairness

## Slide 64: Scheduling of Periodic Tasks
Share of T in ideal schedule in [0,u) = ( )  u.
lag(T, u) = – Pfair(T, u).
If p divides u, then lag is an integer.
  –1< lag < 1  lag = 0.
  Hence, all jobs meet their deadlines.

## Slide 65: More Formal Proof of PFairness

## Slide 66
Pfairness ensured by
  Scheduling subtasks
    Each task is broken into a sequence of quantum-length subtasks.
  Time-driven, quantum-based scheduling
    Scheduling decisions at quantum boundaries.
    Time is integral, measured in units of quanta.
    Interval [i, i+1) – is ith quantum or time slot.
    Schedules at most M subtasks (M – no. of processors).
Task migrations are allowed.

## Slide 67: Scheduling of Subtasks
Each task is effectively divided into a series of quantum-length subtasks.
TIME 1 2 3 4 5 6 7
Subtask 3
Subtask 2
Subtask 1
lag(T, 3) = (3/7)  3 – 0 = 9/7 > 1
So the first subtask must finish by time 3.
lag = 9/7
Consider
a task T of
weight 3/7.

## Slide 68: Scheduling of Subtasks
TIME 1 2 3 4 5 6 7
Subtask 3
Subtask 2
Subtask 1
lag(T, 5) = (3/7)  5 – 1 = 8/7 > 1
So the second subtask must finish by time 5.
lag = 8/7

## Slide 69: Scheduling of Subtasks
TIME 1 2 3 4 5 6 7
Subtask 3
Subtask 2
Subtask 1
lag = –8/7
lag(T, 2) = (3/7)  2 – 2 = –8/7 < –1
So the second subtask cannot be scheduled at time 1.

## Slide 70: Pfair Windows
The lag bounds define evenly-spaced windows in which each subtask must execute.
TIME 1 2 3 4 5 6 7 8 9 10 11 12 13 14
Window 3
Window 2
Window 1
Thus, each subtask has a release-time and a deadline.

## Slide 71: PF Runtime Algorithm

## Slide 72: END

## Slide 73
Demand Bound Function

## Slide 74: Definition of DBF
DBF(Taui, t)=max cumulative execution requirement of jobs of sporadic task Taui in any internal of length t.
load(Tau, t)=
Result: Any sporadic task system Tau is EDF-schedulable on a preemptive uniprocessor if load(Tau) ≤ lne2
Result: Liu and Layland
Result: Any sporadic task system is DM-schedulable on a preemptive uniprocessor if load(Tau) ≤ 0.567 (solution to the equation … )

## Slide 75: Response Time Analysis

## Slide 76: Scheduling Anomaly Example 1
Doubling processor speed causes T1 to miss its deadline
(Yellow part denotes a critical section shared by T1 and T2) _
Notes: This is a good example to show you cannot simply round up exe time to its ceiling in MP scheduling.

## Slide 77: Scheduling Anomaly Example 2
Increasing T1’s period from 4 to 5 causes T1 to miss its deadline
Notes: This is an example to show you cannot take the floor of task period.