## Slide 1: CS252 Graduate Computer Architecture Lecture 23 Graphics Processing Units (GPU) April 18th, 2012
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~kubitron/cs252

## Slide 2: Types of Parallelism
Instruction-Level Parallelism (ILP)
  Execute independent instructions from one instruction stream in parallel (pipelining, superscalar, VLIW)
Thread-Level Parallelism (TLP)
  Execute independent instruction streams in parallel (multithreading, multiple cores)
Data-Level Parallelism (DLP)
  Execute multiple operations of the same type in parallel (vector/SIMD execution)
Which is easiest to program?
Which is most flexible form of parallelism?
  i.e., can be used in more situations
Which is most efficient?
  i.e., greatest tasks/second/area, lowest energy/task

## Slide 3: Remember Vector Computers?
Vectors provide efficient execution of data-parallel loop codes
Vector ISA provides compact encoding of machine parallelism
Vector ISA scales to more lanes without changing binary code
Vector registers provide fast temporary storage to reduce memory bandwidth demands, & simplify dependence checking between vector instructions
Scatter/gather, masking, compress/expand operations increase set of vectorizable loops
Requires extensive compiler analysis (or programmer annotation) to be certain that loops can be vectorized
Full “long” vector support (vector length control, scatter/gather) still only in supercomputers (NEC SX9, Cray X1E); microprocessors have limited packed or subword-SIMD operations
  Intel x86 MMX/SSE/AVX
  IBM/Motorola PowerPC VMX/Altivec

## Slide 4: Multimedia Extensions (aka SIMD extensions)
Very short vectors added to existing ISAs for microprocessors
Use existing 64-bit registers split into 2x32b or 4x16b or 8x8b
  Lincoln Labs TX-2 from 1957 had 36b datapath split into 2x18b or 4x9b
  Newer designs have wider registers
    128b for PowerPC Altivec, Intel SSE2/3/4
    256b for Intel AVX
Single instruction operates on all elements within register
16b
16b
16b
16b
32b
32b
64b
8b
8b
8b
8b
8b
8b
8b
8b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
+
+
+
+
4x16b adds

## Slide 5: Multimedia Extensions versus Vectors
Limited instruction set:
  no vector length control
  no strided load/store or scatter/gather
  unit-stride loads must be aligned to 64/128-bit boundary
Limited vector register length:
  requires superscalar dispatch to keep multiply/add/load units busy
  loop unrolling to hide latencies increases register pressure
Trend towards fuller vector support in microprocessors
  Better support for misaligned memory accesses
  Support of double-precision (64-bit floating-point)
  New Intel AVX spec (announced April 2008), 256b vector registers (expandable up to 1024b)

## Slide 6: Resurgence of DLP
Convergence of application demands and technology constraints drives architecture choice
New applications, such as graphics, machine vision, speech recognition, machine learning, etc. all require large numerical computations that are often trivially data parallel
SIMD-based architectures (vector-SIMD, subword-SIMD, SIMT/GPUs) are most efficient way to execute these algorithms

## Slide 7: DLP important for conventional CPUs too
Prediction for x86 processors, from Hennessy & Patterson, 5th edition
  Note: Educated guess, not Intel product plans!
TLP: 2+ cores / 2 years
DLP: 2x width / 4 years
DLP will account for more mainstream parallelism growth than TLP in next decade.
  SIMD –single-instruction multiple-data (DLP)
  MIMD- multiple-instruction multiple-data (TLP)

## Slide 8: Graphics Processing Units (GPUs)
Original GPUs were dedicated fixed-function devices for generating 3D graphics (mid-late 1990s) including high-performance floating-point units
  Provide workstation-like graphics for PCs
  User could configure graphics pipeline, but not really program it
Over time, more programmability added (2001-2005)
  E.g., New language Cg for writing small programs run on each vertex or each pixel, also Windows DirectX variants
  Massively parallel (millions of vertices or pixels per frame) but very constrained programming model
Some users noticed they could do general-purpose computation by mapping input and output data to images, and computation to vertex and pixel shading computations
  Incredibly difficult programming model as had to use graphics pipeline model for general computation

## Slide 9: General-Purpose GPUs (GP-GPUs)
In 2006, Nvidia introduced GeForce 8800 GPU supporting a new programming language: CUDA
  “Compute Unified Device Architecture”
  Subsequently, broader industry pushing for OpenCL, a vendor-neutral version of same ideas.
Idea: Take advantage of GPU computational performance and memory bandwidth to accelerate some kernels for general-purpose computing
Attached processor model: Host CPU issues data-parallel kernels to GP-GPU for execution
This lecture has a simplified version of Nvidia CUDA-style model and only considers GPU execution for computational kernels, not graphics
  Would probably need another course to describe graphics processing

## Slide 10: Simplified CUDA Programming Model
Computation performed by a very large number of independent small scalar threads (CUDA threads or microthreads) grouped into thread blocks.
// C version of DAXPY loop.
void daxpy(int n, double a, double*x, double*y)
{ for (int i=0; i<n; i++)
y[i] = a*x[i] + y[i]; }
// CUDA version.
__host__ // Piece run on host processor.
int nblocks = (n+255)/256; // 256 CUDA threads/block
daxpy<<<nblocks,256>>>(n,2.0,x,y);
__device__ // Piece run on GP-GPU.
void daxpy(int n, double a, double*x, double*y)
{ int i = blockIdx.x*blockDim.x + threadId.x;
if (i<n) y[i]=a*x[i]+y[i]; }

## Slide 11: Programmer’s View of Execution
blockIdx 0
threadId 0
threadId 1
threadId 255
blockIdx 1
threadId 0
threadId 1
threadId 255
blockIdx
(n+255/256)
threadId 0
threadId 1
threadId 255
Create enough blocks to cover input vector
(Nvidia calls this ensemble of blocks a Grid, can be 2-dimensional)
Conditional (i<n) turns off unused threads in last block
blockDim = 256 (programmer can choose)

## Slide 12: Hardware Execution Model
GPU
GPU is built from multiple parallel cores, each core contains a multithreaded SIMD processor with multiple lanes but with no scalar processor
CPU sends whole “grid” over to GPU, which distributes thread blocks among cores (each thread block executes on one core)
  Programmer unaware of number of cores
Core 0
Lane 0
Lane 1
Lane 15
Core 1
Lane 0
Lane 1
Lane 15
Core 15
Lane 0
Lane 1
Lane 15
GPU Memory
CPU
CPU Memory

## Slide 13: “Single Instruction, Multiple Thread”
GPUs use a SIMT model, where individual scalar instruction streams for each CUDA thread are grouped together for SIMD execution on hardware (Nvidia groups 32 CUDA threads into a warp)
µT0
µT1
µT2
µT3
µT4
µT5
µT6
µT7
ld x
mul a
ld y
add
st y
Scalar instruction stream
SIMD execution across warp

## Slide 14: Implications of SIMT Model
All “vector” loads and stores are scatter-gather, as individual µthreads perform scalar loads and stores
  GPU adds hardware to dynamically coalesce individual µthread loads and stores to mimic vector loads and stores
Every µthread has to perform stripmining calculations redundantly (“am I active?”) as there is no scalar processor equivalent

## Slide 15: Conditionals in SIMT model
Simple if-then-else are compiled into predicated execution, equivalent to vector masking
More complex control flow compiled into branches
How to execute a vector of branches?
µT0
µT1
µT2
µT3
µT4
µT5
µT6
µT7
tid=threadid
If (tid >= n) skip
Call func1
add
st y
Scalar instruction stream
SIMD execution across warp
skip:

## Slide 16: Branch divergence
Hardware tracks which µthreads take or don’t take branch
If all go the same way, then keep going in SIMD fashion
If not, create mask vector indicating taken/not-taken
Keep executing not-taken path under mask, push taken branch PC+mask onto a hardware stack and execute later
When can execution of µthreads in warp reconverge?

## Slide 17: Warps are multithreaded on core
One warp of 32 µthreads is a single thread in the hardware
Multiple warp threads are interleaved in execution on a single core to hide latencies (memory and functional unit)
A single thread block can contain multiple warps (up to 512 µT max in CUDA), all mapped to single core
Can have multiple blocks executing on one core
[Nvidia, 2010]

## Slide 18: GPU Memory Hierarchy
[ Nvidia, 2010]

## Slide 19: SIMT
Illusion of many independent threads
But for efficiency, programmer must try and keep µthreads aligned in a SIMD fashion
  Try and do unit-stride loads and store so memory coalescing kicks in
  Avoid branch divergence so most instruction slots execute useful work and are not masked off

## Slide 20: Nvidia Fermi GF100 GPU
[Nvidia, 2010]

## Slide 21: Fermi “Streaming Multiprocessor” Core

## Slide 22: Fermi Dual-Issue Warp Scheduler

## Slide 23: Apple A5X Processor for iPad v3 (2012)
12.90mm x 12.79mm
45nm technology
[Source: Chipworks, 2012]

## Slide 24: Historical Retrospective, Cray-2 (1985)
243MHz ECL logic
2GB DRAM main memory (128 banks of 16MB each)
  Bank busy time 57 clocks!
Local memory of 128KB/core
1 foreground + 4 background vector processors
Foreground CPU
Shared Memory
Core 0
Lane
Local Memory
Core 0
Lane
Local Memory
Core 0
Lane
Local Memory
Core 0
Lane
Local Memory

## Slide 25: GPU Future
High-end desktops have separate GPU chip, but trend towards integrating GPU on same die as CPU (already in laptops, tablets and smartphones)
  Advantage is shared memory with CPU, no need to transfer data
  Disadvantage is reduced memory bandwidth compared to dedicated smaller-capacity specialized memory system
    Graphics DRAM (GDDR) versus regular DRAM (DDR3)
Will GP-GPU survive? Or will improvements in CPU DLP make GP-GPU redundant?
  On same die, CPU and GPU should have same memory bandwidth
  GPU might have more FLOPS as needed for graphics anyway

## Slide 26: Acknowledgements
These slides contain material developed and copyright by:
  Krste Asanovic (UCB)