## Slide 1: Meltdown & Spectre
20190107

## Slide 2
Meltdown

## Slide 3: Memory Hierarchy
Cache
Small, Fast
(SRAM)
Capacity: register << cache (typically on-chip) << memory (off-chip)
Latency: register << cache (typically on-chip) << memory (off-chip)
On a data access:
  if data Î cache  cache hit  low latency access (SRAM)
  if data Ï cache  cache miss  high latency access (DRAM)
  Goal: create the illusion of accessing as much memory as is available in the slow memory at the speed of the fast cache
CPU
Big, Slow Memory
(DRAM)
holds frequently used data
Registers
Notes: Due to cos t
Due to size of DRAM
Due to cost and wire delays (wires on-chip cost much less, and are faster)
When accessing a memory address, one of two things can happen:
  Cache hit: cache block is valid and refers to the proper memory address, so read from cache (fast)
  Cache miss: cache block is invalid, or refers to the wrong memory address, so read from memory (slow)

## Slide 4: Memory Technologies
Caches use SRAM (Static Random Access Memory) for speed and technology compatibility
  Fast (typical access times of 0.5 to 2.5 ns)
  Low density (6 transistor cells), higher power, expensive
  Static: content will last as long as power is on
Main memory uses DRAM (Dynamic RAM) for size and density
  Slower (typical access times of 50 to 70 ns)
  High density (1 transistor cells), lower power, cheaper
  Dynamic: needs to be “refreshed” regularly (every ~8 ms)
    Consumes 1% to 2% of the active cycles of the DRAM
Notes: Size comparison: DRAM/SRAM is 4 to 8 times
Cost/cycle time comparison SRAM/DRAM is 8 to 16 times
http://parts.digikey.com/1/parts/1211303-ic-sram-1mbit-10ns-32soj-cy7c109d-10vxi.html
Quantity discount 10ns 1MBit SRAM $2.24, $17/Mbyte, $1700/100 Mbyte, $17000/GByte
http://www.frys.com/template/harddrives
DRAM: 4GB @ $70 or $17.50 per GB
24GB@$800 = $33/Gbyte
http://www.frys.com/category/Outpost/Hard+Drives+&+Memory/Memory/Notebook+Memory/Apple+-+Mac++Memory/
DDR2 1GB @ $25 per
DDR3 1 GB @ $37.5 per
FLASH Media
Approx. $2 per Gbyte

## Slide 5
Cache Hierarchy
Larger, slower, cheaper memory, e.g., DRAM
Typical page size: 4KB or larger
Smaller, faster, more expensive memory, e.g., SRAM
Typical block size: 4 – 16 Bytes
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
14
CPU

## Slide 6
Cache Hit
Data in block b is needed
Block b is in cache:
Hit!
Data is loaded from cache into CPU register
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Request: 14
14
CPU

## Slide 7
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)
Data is loaded from cache into CPU register
CPU
Cache Miss

## Slide 8: Memory Hierarchy Speed vs. Size
Second
Level
Cache
(SRAM)
CPU Control
CPU
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s 1,000,000’s
Size (bytes): 100B’s 10KB’s MB’s GB’s TB’s
Cost/bit: highest lowest
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).
Programmer-invisible hardware mechanism gives illusion of speed of fastest memory with size of largest memory
  Works even if you have no idea what a cache is
  Performance-oriented programmers sometimes “reverse engineer” cache organization to design data structures and access patterns optimized for a specific cache design

## Slide 9: How is the Hierarchy Managed?
CPU registers  cache
  By compiler (or assembler programmer)
Cache  main memory
  By the cache controller hardware
  Focus of this lecture
Main memory  hard disk (secondary storage)
  By the OS (virtual memory)
  By the programmer (files)
Notes: Virtual to physical address mapping assisted by the hardware (Translation LB)

## Slide 10: Principle of Locality
Principle of Locality: Programs access small portion of address space at any instant of time (spatial locality) and repeatedly access that portion (temporal locality)
Temporal Locality (locality in time)
  Go back to same book on desk multiple times
  If a memory location is referenced, then it will tend to be referenced again soon
    Keep recently-accessed blocks in the cache
Spatial Locality (locality in space)
  When go to book shelf, pick up multiple books around the book you want, since library stores related books together
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon
    When fetching a block into cache, also fetch blocks around it
Notes: How does the memory hierarchy work? Well it is rather simple, at least in principle.
In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.
+1 = 15 min. (X:55)

## Slide 11: Quiz: What locality does this program have?
Data:
  Temporal locality: variable sum is referenced in each iteration
  Spatial locality: array a[] is accessed with stride-1 in each iteration (assuming a[] is stored in contiguous addresses in memory)
Instructions:
  Temporal locality: the loop body is executed repeatedly for n times
  Spatial locality: instructions are accessed sequentially (with 1 branch in each iteration) (assuming instructions are stored in contiguous addresses in memory)
int sum = 0, a[n];
…
for (i = 0; i < n; i++) {
sum += a[i];
}
return sum;

## Slide 12
Meltdown

## Slide 13: Flush-and-Reload Cache Side Channel Analysis
Suppose victim holds some secret value x
Attacker constructs array[N*STEP], where x<N, and flushes the entire array to memory
Let the victim access element array[x*STEP] to bring it into cache
Attacker reloads array[0*STEP], array[1*STEP],…,array[(N-1)*STEP] array[N*STEP] by reading them in sequence, and measures access time of each element. Only accessing array[x*STEP] should be a cache hi t. This reveals the secret x
STEP should be much larger than cache block size, so that no two different elements array[i*STEP] and array[j*STEP] will be in the same cache block; also to remove the effect of cache prefetching, where multiple cache blocks are brought into memory upon a cache miss
a[0*STEP] | a[0*STEP+1] | a[0*STEP+2] | a[0*STEP+3] | a[0*STEP+4]
a[1*STEP] | a[1*STEP+1] | a[1*STEP+2] | a[1*STEP+3] | a[1*STEP+4]
a[2*STEP] | a[2*STEP+1] | a[2*STEP+2] | a[2*STEP+3] | a[2*STEP+4]
a[3*STEP] | a[3*STEP+1] | a[3*STEP+2] | a[3*STEP+3] | a[3*STEP+4]
a[4*STEP] | a[4*STEP+1] | a[4*STEP+2] | a[4*STEP+3] | a[4*STEP+4]
Suppose cache block size is 2, STEP=5; Victim accesses a[2*5], causing cache block containing a[10] and a[11] to be brought into cache. Attacker reloads 5 elements in the 1st column, and finds out that only accessing a[10] is a cache hit

## Slide 14: Virtual Memory
Each process sees a continuous virtual address space with size 2N Bytes (N=16, 32, 64…)
Part of the address range is user-space, accessible by both user processes and OS kernel
Part of the address range is kernel-space, accessible by the OS kernel
Security isolation: user processes should not be able to access kernel-space

## Slide 15: Meltdown attack
Page table maps from virtual address to physical address
A user can use Meltdown attack to break security isolation, and access kernel memory space
Access permission check should fail, so the next line should not be executed. But Meltdown breaks this

## Slide 16: array[] in memory and cache
Each memory page is 4KB (STEP=4096 Bytes).
Each cache block is 64 Bytes
array[] contains 10 pages (40KB) of 8-Byte elements, each page has starting address of 0*4096, 1*4096, …., 9*4096.
Notes: Accessing 2 elements of array[] to bring them into cache, causes future accesses to these 2 elements

## Slide 17: Listing 1: CacheTime.c
Access 2 elements of array[] to bring them into cache
Subsequent accesses to these elements will be cache hits and will be much faster
Notes: Accessing 2 elements of array[] to bring them into cache, causes future accesses to these 2 elements

## Slide 18: Cache size channel attack: FLUSH+RELOAD
1. FLUSH the entire array from the cache to make sure the array is not cached.
2. Invoke the victim function, which accesses one of the array elements based on the value of the secret. This action causes the corresponding array element to be cached.
3. RELOAD the entire array, and measure the time it takes to reload each element. Loading element corresponding to the secret element will be a cache hit, and be much faster.

## Slide 19: Listing 2: FlushReload.c
Since array[0*4096] may fall into the same cache block as the variables in adjacent memory (with address lower than array[0]), it may be accidentally cached due to the caching of those variables.
Therefore, we use array[k*4096 + DELTA] for all k values, where DELTA is defined as a constant 1024

## Slide 20: Task 3: Place Secret Data in Kernel Space
Listing 3: MeltdownKernel.c
Line 1: saves the address of the secret data into the kernel message buffer ()
Use the secret once to bring it into cache
Line 3: create a data entry /proc/secret_data. When a user-level program reads from this entry, the read proc() function in the kernel module will be invoked, inside which, the secret variable will be loaded (Line 1) and thus be cached by the CPU

## Slide 21: Finding the secret data address
After compilation, use the insmod command to install the kernel module, then use the dmesg command to find the secret data’s address from the kernel message buffer.

## Slide 22: Task 4: Access Kernel Memory from User Space
This program will crash, since you are trying to access kernel memory from user space
Replace this address with the address obtained from Task 3

## Slide 23: Task 5: Handle Error/Exceptions in C
Instead of program crashing, we want to print out a message “"Memory access violation!”
To catch the exception SIGSEGV caused by accessing kernel memory address from user space, we emulate the try/catch clause in C++ using sigsetjmp() and siglongjmp(),

## Slide 24: Out-of-Order Execution
Line 3 involves two operations at Assembly code level:
  3.A Load the data into cache and then into CPU register
  3.B check the data access permission, and if permission check fails, roll back any instructions (e.g., instruction 4) executed after the check
In-order execution: instructions 3.A, 3.B and 4 execute in order
Out-of-Order Execution: instruction 3.A executes first, then instructions 3.B and 4 execute in parallel in the CPU pipeline (since both 3.B and 4 depend on “kernel_data” loaded by 3.A)
3A
3B
4

## Slide 25: Meltdown Attack
Race condition between 3B and 4; either one may execute first
  If instruction 3B executes before 4, and permission check fails, then 4 will not execute at all
  If instruction 4 executes speculatively before 3B, and permission check fails, then roll back any effect of 4
The rolled-back instructions do not have any externally visible effect: variable “number” stays unchanged
However, “kernel_data”, the data stored at memory address “kernel_address”, has been brought into the cache (and CPU register), and attacker can find its value by cache side channel analyiss
Accessing kernel data (3A)
Permission check (3B)
Inst. that brings kernel data into cache (4)
They will be rolled back if permission check fails

## Slide 26: MeltdownExperiment.c
Line 2: array[7 * 4096 + DELTA] will be loaded into the CPU cache due to Out-of-Order execution, but a memory access violation will occur subsequently, so its value will not be actually incremented at the end
Replace this address with the address obtained from Task 3

## Slide 27: Task 7.1: The Basic Meltdown Attack
Instead of array[7 * 4096 + DELTA], we access array[kernel_data * 4096 + DELTA]
Using the FLUSH+RELOAD technique, we check the access time of array[i*4096 + DELTA] for i = 0, . . ., 255.
If we find out that only array[k*4096 + DELTA] is in the cache, we can infer that the value of the “kernel_data” is k.

## Slide 28: Task 7.2: Improve the Attack by Getting the Secret Data Cached
To maximize chance of success of attack, we can preload the kernel secret data into cache before launching the attack
The following user-level program uses system calls open() and pread() to access the secret data without leaking it to the user-level program by reading 0 bytes into a NULL buffer
  ssize_t pread(int fildes, void *buf, size_t nbyte, off_t offset);
Notes: ssize_t pread(int fildes, void *buf, size_t nbyte, off_t offset);

## Slide 29: Task 7.3: Using Assembly Code to Trigger Meltdown
To maximize chance of success, Meltdown_asm() runs a useless computation loop for 400 times, in order to occupy the ALUs to delay execution of Permission check, making it more likely to execute *after* instruction 4
Accessing kernel data (3A)
Permission check (3B)
Inst. that brings kernel data into cache (4)
Useless Computation
Delays

## Slide 30: Task 8: Make the Attack More Practical
The actual timing measurements may be noisy due to cache prefetching, OS scheduling, interrupts and other interference effects, making it difficult to set the proper value of CACHE_HIT_THRESHOLD that works always
Statistical technique: create a score array of size 256, one element for each possible secret value. We then run our attack for 1000 times. Each time, if our attack program says that k is the secret (this result may be false), we add 1 to scores[k]. After running the attack for many times, we use the value k with the highest score as our final estimation of the secret

## Slide 31: Statistical technique

## Slide 32
Spectre

## Slide 33: Non-Pipelined Instruction Execution (hypothetical)
2nd Instruction (Adrs: PC+2)
Fetch
Decode
Execute
1st Instruction (Adrs: PC)
Fetch
Decode
Execute
3rd Instruction (Adrs: PC+4)
Fetch
Decode
Execute
Time
One instruction completed every 3 cycles. Performance is much lower than pipelined execution.
Fetch
Decode
Execute
PC
PC - 2
PC - 4

## Slide 34: Pipelined Instruction Execution
Fetch
Decode
Execute
PC
PC - 2
PC - 4
2nd Instruction (Adrs: PC+2)
Fetch
Decode
Execute
1st Instruction (Adrs: PC)
Fetch
Decode
Execute
3rd Instruction (Adrs: PC+4)
Fetch
Decode
Execute
Time
Pipelining allows multiple instructions to be in progress simultaneously during any one processor clock cycle. While one instruction is fetched, another is decoded, and a third is executed.
Notes: Thumb instructions are 16 or 32 bits wide, with the majority being 16 bits. Thus, while the address held in PC is being used to read one 16-bit instruction from memory, the previous instruction (from address PC-2) is decoded, and the one before that (from address PC-4) is executed. One instruction completed every cycle.

## Slide 35: Out-of-Order Execution (or Speculative Execution)
Predict branch direction
Go Faster: Pipelining, branch prediction, & instruction speculation
add
load
branch
and
Speculate!
store
Speculate more!
Speculation correct: Commit architectural changes of and (register) & store (memory) instructions
Mis-speculate: Abort architectural changes (registers, memory); go in other branch direction

## Slide 36: Out-of-Order Execution Example
In-order execution: Line 3 (data = data + 5) is executed only if condition (x < size) is true
Out-of-order execution: Line 3 may be executed speculatively before condition (x < size) is checked; its effects will be rolled back if (x < size) is false
  Condition check may be slow if x is in memory (not in cache)
  The CPU branch predictor predicts direction of each branch, and the predicted branch is executed speculatively before condition is checked
  If branch prediction is wrong, the speculative execution is rolled back, and the correct branch will be executed
data = 0;
check (if x < size)
data = data +5

## Slide 37: Listing 3: SpectreExperiment.c
The for loop starting from Line 3 invokes victim() with a small argument (from 0 to 9). These values are less than the value size, so the true-branch of the if-condition in Line 1 is always taken. This is the training phase, which essentially trains the CPU to expect the if-condition to be “true”.
Once the CPU is trained, we pass a larger value (97) to the victim() function (Line 5). This value is larger than size, so the false-branch of the if-condition inside victim() will be taken.
However, we have flushed the variable “size” from the cache, so the check “if x < size” will be slow due to memory access. Line 2 will be executed speculatively based on branch prediction of “true”

## Slide 38: Task 4: The Spectre Attack
True-branch will never be executed if x is larger than the buffer size,
But at microarch level, it can be executed speculatively. Even though it will be rolled back later, the cache state has been altered and can be attacked
Notes: and some traces can be left behind when the execution is rolled back

## Slide 39: Recall: Stack Overflow Attack
(a) Situation when main program is running
(b) After procedure A() called
(c) Buffer overflow alters the return address from A().
  Can be garbage that causes program crash, or can be address of a malicious program
Checking array bounds (if (x < buffer_size)) prevents stack overflow attack, but not Spectre attack due to cache side channel

## Slide 40: Listing 4: SpectreAttack.c
Line 4 calculates the offset of the secret from the beginning of the buffer
The offset larger_x is larger than 10, and is fed into the restrictedAccess() function
“return buffer[x]” will be executed speculatively to return buffer[larger x], which contains the value of the secret. Its effects will be rolled back later, and the correct branch “return 0” will be executed, but buffer[larger x] is left in the cache, and attacker can find it with cache side channel

## Slide 41: Task 5: Improve the Attack Accuracy
Statistical technique: create a score array of size 256, one element for each possible secret value. We then run our attack for 1000 times. Each time, if our attack program says that k is the secret (this result may be false), we add 1 to scores[k]. After running the attack for many times, we use the value k with the highest score as our final estimation of the secret
“You may observe that when running the code above, the one with the highest score is always scores[0]. Please figure out the reason, and fix the code above, so the actual secret value (which is not zero) will be printed out.”
  Gu: I do not understand this part. Anyone can help?

## Slide 42: Task 6: Steal the Entire Secret String
Hint:
char *secret = "Some Secret Value";
  secret is a pointer to the memory address of the 0th array element secret[0] (‘S’)
  Secret+1 is a pointer to the memory address of the 1st array element secret[1] ‘o’
  …

## Slide 43: Meltdown vs. Spectre
Meltdown: an instruction accessing kernel memory causes an exception, but subsequent operations are executed speculatively, and bring array[x*STEP] into cache
The speculative execution is rolled back upon the exception, but cache state is altered
Spectre: a branch condition should prevent execution of certain instructions, but subsequent operations in the wrong branch are executed speculatively, and bring array[x*STEP] into cache
The speculative execution is rolled back upon getting the actual branch condition, but cache state is altered
(Assume each instruction is 16 bits (2 Bytes), hence the next instruction is n+2)