## Slide 1: On the Meltdown & Spectre Design Flaws
Mark D. Hill
Computer Sciences Dept.
Univ. of Wisconsin-Madison
February 2018
Computer Architect, Not Security Expert
Prepared while on a sabbatical visit to Google with public information only and representing the author’s views only, not necessarily Google’s.

## Slide 2: Talk Info (Hidden Slide)
Title: On the Meltdown & Spectre Design Flaws
Speaker: Mark D. Hill, Computer Sciences Department, University of Wisconsin-Madison
Abstract: Two major hardware security design flaws--dubbed Meltdown and Spectre--were broadly revealed to the public in early January 2018 in research papers and blog posts that require considerable expertise and effort to understand. To complement these, this talk seeks to give a general computer science audience the gist of these security flaws and their implications. The goal is to enable the audience can either stop there or have a framework to learn more. A non-goal is exploring many details of flaw exploitation and patch status, in part, because the speaker is a computer architect, not a security expert. In particular, this talk reviews that Computer Architecture 1.0 (the version number is new) specifies the timing-independent functional behavior of a computer and micro-architecture that is the set of implementation techniques that improve performance by more than 100x. It then asks, “What if a computer that is completely correct by Architecture 1.0 can be made to leak protected information via timing, a.k.a., micro-architecture?” The answer is that this exactly what is done by the Meltdown and Spectre design flaws. Meltdown leaks kernel memory, but software & hardware fixes exist. Spectre leaks memory outside of sandboxes and bounds check, and it is scary. An implication is that the definition of Architecture 1.0--the most important interface between software and hardware--is inadequate to protect information. It is time for experts from multiple viewpoints to come together to create Architecture 2.0).
Bio: Mark D. Hill (http://www.cs.wisc.edu/~markhill) is John P. Morgridge Professor and Gene M. Amdahl Professor of Computer Sciences at the University of Wisconsin-Madison. Hill has a PhD in computer science from the University of California, Berkeley. Hill’s research targets computer design and evaluation. He has made contributions to parallel computer system design (e.g., memory consistency models and cache coherence), memory system design (caches and translation buffers), computer simulation (parallel systems and memory systems), software (e.g., page tables and cache-conscious optimizations), deterministic replay and transactional memory. For example, he is the inventor of the widely-used 3C model of cache behavior (compulsory, capacity, and conflict misses) and co-inventor of the cornerstone for the C++ and Java multi-threaded memory specifications (sequential consistency for data-race-free programs). He is a fellow of IEEE and the ACM. He serves as Vice Chair of the Computer Community Consortium (2016-18) and served as Wisconsin Computer Sciences Department Chair 2014-2017.

## Slide 3: Executive Summary
Architecture 1.0: the timing-independent functional behavior of a computer Micro-architecture: the implementation techniques to improve performance
Question: What if a computer that is completely correct by Architecture 1.0 can be made to leak protected information via timing, a.k.a., Micro-Architecture?
Meltdown leaks kernel memory, but software & hardware fixes exist
Spectre leaks memory outside of bounds checks or sandboxes, and is scary
Implication: The definition of Architecture 1.0 is inadequate to protect information

## Slide 4: Outline
Computer Architecture & Micro-Architecture Background
Timing Side-Channel Attack
Meltdown
Spectre
Wrap-Up

## Slide 5: Computer Architecture 0.0 -- Pre-1964
Software Lagged Hardware
Each new machine design was different
Software needed to be rewritten in assembly/machine language
Unimaginable today
Going forward: Need to separate HW interface from implementation
Each Computer was New
Implemented machine (has mass) → hardware
Instructions for hardware (no mass) → software

## Slide 6: Computer Architecture 1.0 -- Born 1964
IBM System 360 defined an instruction set architecture
Stable interface across a family of implementations
Software did NOT have to be rewritten
Architecture 1.0: the timing-independent functional behavior of a computer Micro-architecture: implementation techniques that change timing to go fast
branch (R1 >= bound) goto error
load R2 ← memory[train+R1]
and R3 ← R2 && 0xffff
load R4 ← memory[save+SIZE+R3]
Note: The code is not IBM 360 assembly, but is the example used later.

## Slide 7: Micro-architecture Harvested Moore’s Law Bounty
For decades, every ~2 years: 2x transistors, 1.4x faster & 1x chip power possible; 2300 transistors for Intel 4004 → millions per core & billions for caches
(Micro-)architects took this ever doubling budget to make each processor core execute > 100x than what it would otherwise.
Key techniques w/ tutorial next:
Instruction Speculation
Hardware Caching
Hidden by Architecture 1.0: timing-independent functional behavior unchanged

## Slide 8: Instruction Speculation Tutorial
Many steps (cycles) to execute one instruction; time flows left to right →
add
Predict direction: target or fall thru
Go Faster: Pipelining, branch prediction, & instruction speculation
add
load
branch
and
Speculate!
store
Speculate more!
load
Speculation correct: Commit architectural changes of and (register) & store (memory) go fast!
Mis-speculate: Abort architectural changes (registers, memory); go in other branch direction

## Slide 9: Hardware Caching Tutorial
Main Memory (DRAM) 1000x too slow
Add Hardware Cache(s): small, transparent hardware memory
Like a software cache: speculate near-term reuse (locality) is common
Like a hash table: an item (block or line) can go in one or few slots
E.g., 4-entry cache w/ slot picked with address (key) modulo 4
--
0
--
1
--
2
--
3
12?
Miss
Insert 12
12
0
--
1
--
2
--
3
07?
Miss
Insert 07
12
0
--
1
--
2
07
3
12?
HIT!
No changes
12
0
--
1
--
2
07
3
16?
Miss
Victim 12
Insert 16
16
0
--
1
--
2
07
3
Note 12
victimized “early” due to “alias”

## Slide 10: Micro-architecture Harvested Moore’s Law Bounty
For decades, every ~2 years: 2x transistors, 1.4x faster & 1x chip power possible; 2300 transistors for Intel 4004 → millions per core & billions for caches
(Micro-)architects took this ever doubling budget to make each processor core execute > 100x what it would otherwise
Hidden by Architecture 1.0: timing-independent functional behavior unchanged
branch (R1 >= bound) goto error ; Speculate branch not taken
load R2 ← memory[train+R1] ; Speculate load & speculate cache hit
and R3 ← R2 && 0xffff ; Speculate AND
load R4 ← memory[save+SIZE+R3] ; Speculate load & speculate cache hit

## Slide 11: Whither Computer Architecture 1.0?
Architecture 1.0: timing-independent functional behavior Question: What if a computer that is completely correct by Architecture 1.0 can be made to leak protected information via timing, a.k.a., micro-architecture? Implication: The definition of Architecture 1.0 is inadequate to protect information This is what Meltdown and Spectre do. Let's see why and explore implications.

## Slide 12: Side-Channel Attack: SAVE Secret in Micro-Arch
Prime micro-architectural state
  Repeatedly access array train[]to train branch predictor to expect access < bound
  Access all of array save[]to put it completely in a cache of size SIZE
Coerce processor into speculatively executing instructions that will be nullified to (a) find a secret & (b) save it in micro-architecture
branch (R1 >= bound) goto error ; Speculate not taken even if R1 >= bound
load R2 ← memory[train+R1] ; Speculate to find SECRET outside of train[]
and R3 ← R2 && 0xffff ; Speculate to convert SECRET bits into index
load R4 ← memory[save+SIZE+R3] ; Speculate to save SECRET by victimizing memory[save+R3] since it aliases in cache with new access memory[save+SIZE+R3]
3. HW detects mis-speculation Undoes architectural changes Leaves cache (micro-architecture) changes (correct by Architecture 1.0)

## Slide 13: Side-Channel Attack: RECALL Secret from Micro-Arch
4: Probe time to access each element of save[]--micro-architectural property; If accessing save[foo] slow due to cache miss, then SECRET is foo. A leak! 5: Repeat many times to obtain secret information at some bandwidth. (More shifting/masking needed to get all SECRET bits victimizing 64B cache lines)
Well-known in 1983/85 DoD “Orange Book” Covert timing channels include all vehicles that would allow one process to signal information to another process by modulating its own use of system resources in such a way that the change in response time observed by the second process would provide information. --TRUSTED COMPUTER SYSTEM EVALUATION CRITERIA
With roots back to 1974 TENEX password attack But seemed fanciful
Spy vs. Spy, Mad Magazine, 1960

## Slide 14: Meltdown (https://meltdownattack.com/meltdown.pdf)
Can leak the contents of kernel memory at up to 500KB/s
TRAP!! (not branch)
Under mis-speculation

## Slide 15: Meltdown & Hardware
Demonstrated for many Intel x86-64 cores; NOT demonstrated for AMD
Key: When to suppress load with protection violation (user load to kernel memory)
EARLY: AMD appears to suppress early, e.g., at TLB access
LATE: Intel appears to suppress at end after micro-arch state changes
My SWAG (Scientific Wild A** Guess) Why
Both are correct by Architecture 1.0
Performance shouldn’t matter as this case is supposed to be rare
Do what’s easiest & have luck that is good (AMD) or bad (Intel)

## Slide 16: Meltdown & Software
Bad: Meltdown operates with bug-free OS software (by Architecture 1.0)
Good: Major commercial OSs patched for Meltdown ~January 2018
Idea: Don’t map (much) of protected kernel address space in user process
Offending load now fails address translation & does nothing
Patches quickly derived from KAISER developed for side-channel attacks of Kernel Address Space Layout Randomization (KASLR)
Performance impact 0-30% syscall frequency & core model.
Future hardware can fix Meltdown (like AMD) so maybe we dodged a bullet

## Slide 17: Spectre (https://spectreattack.com/spectre.pdf)
Classic side-channel attack w/ deep micro-arch info
1. Attacker primes micro-architecture
  E.g, branch predictor or branch target buffer for saving secret
  E.g., cache for recalling secret
2: Victim loads secret under mis-speculation
  Load should NOT trap (unlike Meltdown)
  Still inappropriate if managed language or sandbox
3: Victim saves secret in micro-arch state, e.g., cache
4: Attacker recalls secret from micro-arch state; 4: repeat.

## Slide 18: Spectre Applicability (Paper Sections 4, 5, & 6)
4. Exploit branch mis-prediction to let Javascript steal from Chrome browser
Demonstrated Intel Haswell/Skylake, AMD Ryzen, & several ARM cores
Many other existing designs vulnerable
5. Used indirect branches & return-oriented programming to mis-train branch target buffer to obtain information from different hyper-thread on same core
6. Many other known timing-channel exist, e.g., register file contention, functional unit occupancy, but what about unknown timing channels?

## Slide 19: Spectre Mitigation (Section 7)
Branch prediction
SW: Suppress branch prediction “when important” with mfence, etc.
Not defined to work but appears to work--at a performance cost
HW could auto-magically suppress branch prediction when appropriate (???)
Branch Target Buffer
SW: Not clear. Disable hyper-threading, etc.?
HW: Make micro-architecture state private to thread (not core or processor)
More generally: Hard to mitigate threats NOT YET DEFINED.

## Slide 20: Need Computer Architecture 2.0?
With Meltdown & Spectre, Architecture 1.0 is inadequate to protect information
Augment Architecture 1.0 with Architecture 2.0 specification of
(Abstraction of) time-visible micro-architecture?
Bandwidth of known (unknown?) timing channels?
Enforced limits on user software behavior? (c.f., KAISER)
Change Microarchitecture to mitigate timing channel bandwidth
Suppress some speculation
Undo most changes on mis-speculation
Can this be (formally) solved or must it be managed like crime?

## Slide 21: Need Computer Architecture 2.0?
More generally, can we reduce our dependence on SPECULATION?
Accelerators!! GPU, DSP, IPU, TPU, ... [Hennessy & Patterson 2018 Taxonomy]
Dedicated Memories
More ALUs
Easy Parallelism
Lower precision data
Domain Specific Language
Yavits et al. MultiAmdahl, 2017
Speculation NOT a first-order feature!
In 2005, Arvind said Speculation (w/ von Neumann model) killed Dataflow
After 2018, Dataflow-like Renaissance w/ Sea of Accelerators?

## Slide 22: Executive Summary
Architecture 1.0: the timing-independent functional behavior of a computer Micro-architecture: the implementation techniques to improve performance
Question: What if a computer that is completely correct by Architecture 1.0 can be made to leak protected information via timing, a.k.a., Micro-Architecture?
Implication: The definition of Architecture 1.0 is inadequate to protect information
Meltdown leaks kernel memory, but software & hardware fixes exist
Spectre leaks memory outside of bounds checks or sandboxes, and is scary

## Slide 23: Some References
New York Times: https://www.nytimes.com/2018/01/03/business/computer-flaws.html Meltdown paper: https://meltdownattack.com/meltdown.pdf Spectre paper: https://spectreattack.com/spectre.pdf A blog separating the two bugs: https://danielmiessler.com/blog/simple-explanation-difference-meltdown-spectre/ Google Blog: https://security.googleblog.com/2018/01/todays-cpu-vulnerability-what-you-need.html and https://googleprojectzero.blogspot.com/2018/01/reading-privileged-memory-with-side.html Industry News Sources: https://arstechnica.com/gadgets/2018/01/whats-behind-the-intel-design-flaw-forcing-numerous-patches/ and https://www.theregister.co.uk/2018/01/02/intel_cpu_design_flaw/

## Slide 24: Backup Slides

## Slide 25: Spectre Code Example
Listing 2: Exploiting Speculative Execution via JavaScript
1 if (index < simpleByteArray.length) {
2 index = simpleByteArray[index | 0];
3 index = (((index * TABLE1_STRIDE)|0) & (TABLE1_BYTES-1))|0;
4 localJunk ^= probeTable[index|0]|0;
5}
Listing 3: Disassembly of Speculative Execution in Listing 2 JavaScript
1 cmpl r15,[rbp-0xe0] ; Compare index (r15) against simpleByteArray.length
2 jnc 0x24dd099bb870 ; If index >= length, branch to instruction after move below
3 REX.W leaq rsi,[r12+rdx*1] ; Set rsi=r12+rdx=addr of first byte in simpleByteArray
4 movzxbl rsi,[rsi+r15*1] ; Read byte from address rsi+r15 (= base address+index)
5 shll rsi, 12 ; Multiply rsi by 4096 by shifting left 12 bits}\%\
6 andl rsi,0x1ffffff ; AND reassures JIT that next operation is in-bounds
7 movzxbl rsi,[rsi+r8*1] ; Read from probeTable
8 xorl rsi,rdi ; XOR the read result onto localJunk
9 REX.W movq rdi,rsi ; Copy localJunk into rdi

## Slide 26: Meltdown v. Spectre
Miessler Blog (https://danielmiessler.com/blog/simple-explanation-difference-meltdown-spectre/ )