## Slide 1: Meltdown & Spectre
201906

## Slide 2
Meltdown

## Slide 3: Memory Hierarchy
Cache
Small, Fast
(SRAM)
Capacity: register << cache (typically on-chip) << memory (off-chip)
Latency: register << cache (typically on-chip) << memory (off-chip)
On a data access:
  if data Î cache  cache hit  low latency access (SRAM)
  if data Ï cache  cache miss  high latency access (DRAM)
  Goal: create the illusion of accessing as much memory as is available in the slow memory at the speed of the fast cache
CPU
Big, Slow Memory
(DRAM)
holds frequently used data
Registers
Notes: Due to cost
Due to size of DRAM
Due to cost and wire delays (wires on-chip cost much less, and are faster)
When accessing a memory address, one of two things can happen:
  Cache hit: cache block is valid and refers to the proper memory address, so read from cache (fast)
  Cache miss: cache block is invalid, or refers to the wrong memory address, so read from memory (slow)

## Slide 4: Memory Technologies
Caches use SRAM (Static Random Access Memory) for speed and technology compatibility
  Fast (typical access times of 0.5 to 2.5 ns)
  Low density (6 transistor cells), higher power, expensive
  Static: content will last as long as power is on
Main memory uses DRAM (Dynamic RAM) for size and density
  Slower (typical access times of 50 to 70 ns)
  High density (1 transistor cells), lower power, cheaper
  Dynamic: needs to be “refreshed” regularly (every ~8 ms)
    Consumes 1% to 2% of the active cycles of the DRAM
Notes: Size comparison: DRAM/SRAM is 4 to 8 times
Cost/cycle time comparison SRAM/DRAM is 8 to 16 times
http://parts.digikey.com/1/parts/1211303-ic-sram-1mbit-10ns-32soj-cy7c109d-10vxi.html
Quantity discount 10ns 1MBit SRAM $2.24, $17/Mbyte, $1700/100 Mbyte, $17000/GByte
http://www.frys.com/template/harddrives
DRAM: 4GB @ $70 or $17.50 per GB
24GB@$800 = $33/Gbyte
http://www.frys.com/category/Outpost/Hard+Drives+&+Memory/Memory/Notebook+Memory/Apple+-+Mac++Memory/
DDR2 1GB @ $25 per
DDR3 1 GB @ $37.5 per
FLASH Media
Approx. $2 per Gbyte

## Slide 5
Cache Block
Cache Hierarchy
Larger, slower, cheaper memory, e.g., DRAM
Typical page size: 4KB or larger
Smaller, faster, more expensive memory, e.g., SRAM
Typical cache block size: 16-64 Bytes
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
14
CPU
Memory Page
Hard Disk
Register
Typical CPU register size: 4 Bytes

## Slide 6: How is the Hierarchy Managed?
Registers  memory hierarchy
  By compiler (or assembler programmer)
Cache  main memory
  By the cache controller hardware
  Focus of this lecture
Main memory  disks (secondary storage)
  By the operating system (virtual memory)
  By the programmer (files)
Notes: Virtual to physical address mapping assisted by the hardware (Translation LB)

## Slide 7: Principle of Locality
Principle of Locality: Programs access small portion of address space at any instant of time (spatial locality) and repeatedly access that portion (temporal locality)
Temporal Locality (locality in time)
  If a memory location is referenced, then it will tend to be referenced again soon
    Keep recently-accessed blocks in the cache
Spatial Locality (locality in space)
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon
    Cache prefetching: when fetching a block into cache, also fetch nearby blocks based on recent block access pattern
Notes: How does the memory hierarchy work? Well it is rather simple, at least in principle.
In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.
+1 = 15 min. (X:55)

## Slide 8: Quiz: What locality does this program have?
Data:
  Temporal locality: variable sum is referenced in each iteration
  Spatial locality: array a[] is accessed with stride-1 in each iteration (assuming a[] is stored in contiguous addresses in memory)
Instructions:
  Temporal locality: the loop body is executed repeatedly for n times
  Spatial locality: instructions are accessed sequentially (with 1 branch in each iteration) (assuming instructions are stored in contiguous addresses in memory)
int sum = 0, a[n];
…
for (i = 0; i < n; i++) {
sum += a[i];
}
return sum;

## Slide 9: Flush-and-Reload Cache Side Channel Analysis
Suppose victim holds some secret value x
Attacker constructs probe array[N*STEP], where x<N, and flushes the entire array to memory
Let the victim access element array[x*STEP] to bring it into cache
Attacker reloads elements array[0*STEP], array[1*STEP],…, array[(N-1)*STEP] by reading them in sequence, and measures access time of each element. Only accessing array[x*STEP] should be a cache hit. This reveals the secret x
STEP should be much larger than cache block size:
  No two different elements array[i*STEP] and array[j*STEP] are in the same cache block
  To mitigate the effect of cache prefetching, where multiple cache blocks are brought into cache upon a cache miss
Measurement results with only one cache hit

## Slide 10: Flush-and-Reload Toy Example
Suppose cache block size is 2 Bytes, STEP=6.
Attacker constructs probe array[5*STEP]; Victim holds secret value x=2, and accesses a[2*5], causing cache block containing elements {a[10], a[11]} to be brought into cache. Attacker reloads 5 elements a[0*STEP]…a[4*STEP], and finds out that only accessing a[10] is a cache hit, so he can deduce the secret x=2.
STEP should be much larger than cache block size
  If the cache prefetching algorithm brings 4 blocks into the cache when accessing a[2*5], including a[3*5], then attacker cannot decide if x=2 or 3.
a[0*STEP] | a[0*STEP+1] | a[0*STEP+2] | a[0*STEP+3] | a[0*STEP+4] | a[0*STEP+5]
a[1*STEP] | a[1*STEP+1] | a[1*STEP+2] | a[1*STEP+3] | a[1*STEP+4] | a[1*STEP+5]
a[2*STEP] | a[2*STEP+1] | a[2*STEP+2] | a[2*STEP+3] | a[2*STEP+4] | a[2*STEP+5]
a[3*STEP] | a[3*STEP+1] | a[3*STEP+2] | a[3*STEP+3] | a[3*STEP+4] | a[3*STEP+5]
a[4*STEP] | a[4*STEP+1] | a[4*STEP+2] | a[4*STEP+3] | a[4*STEP+4] | a[4*STEP+5]
Reloaded Elements
Cache block accessed
by victim;
Fast reload by attacker

## Slide 11: An Analogy of Flush-and-Reload
Imagine that you (i.e. a malicious process) want to know whether someone (i.e. a victim process) has checked out a particular library book. The library (i.e. the CPU) refuses to give you access to their records and does not keep a slip inside the front cover. You can only see the record of which books you have checked out. What you do is follow the person of interest into the library whenever they return a book. You then ask the librarian for a copy of the books you want to know whether the person has checked out. If the librarian looks down and says "You are in luck, I have a copy right here!" then you know the person had checked out that book. If the librarian has to go look in the stacks and comes back 5 minutes later with the book, you know that the person didn't check out that book (this time). The way to make the library secure against this kind of attack is to require that all books be reshelved before they can be lent out again, unless the current borrower is requesting an extension. There are many other ways to use the behavior of the librarian and the time it takes to retrieve a book to figure out which books a person is reading.

## Slide 12
Meltdown

## Slide 13: Virtual Memory
Each process sees a continuous virtual address space with size 2N Bytes (N=16, 32, 64…)
Part of the address range is user-space, accessible by both user processes and OS kernel
Part of the address range is kernel-space, accessible by the OS kernel
Security isolation: user processes should not be able to access kernel-space

## Slide 14: Meltdown attack
Page table maps from virtual address to physical address
A user can use Meltdown attack to break security isolation, and access kernel memory space
Access permission check should fail, so the next line should not be executed. But Meltdown breaks this

## Slide 15: Meltdown Lab Tasks
Tasks 1 and 2: Side Channel Attacks via CPU Caches
  Task 1: Reading from Cache versus from Memory
  Task 2: Using Cache as a Side Channel
Tasks 3-5: Preparation for the Meltdown Attack
  Task 3: Place Secret Data in Kernel Space
  Task 4: Access Kernel Memory from User Space
  Task 5: Handle Error/Exceptions in C
Task 6: Out-of-Order Execution by CPU
Task 7: The Basic Meltdown Attack
  Task 7.1: A Naive Approach
  Task 7.2: Improve the Attack by Getting the Secret Data Cached
  Task 7.3: Using Assembly Code to Trigger Meltdown
Task 8: Make the Attack More Practical

## Slide 16: Task 1: Reading from Cache versus from Memory
Access 2 elements of array[] to bring them into cache
Subsequent accesses to these elements will be cache hits and will be much faster
Listing 1: CacheTime.c
Notes: Accessing 2 elements of array[] to bring them into cache, causes future accesses to these 2 elements

## Slide 17: array[] in memory and cache
Each memory page is 4KB (STEP=4096 Bytes).
Each cache block is 64 Bytes
array[] contains 10 pages (40KB) of 1-Byte elements, each page has starting address of 0*4096, 1*4096, …., 9*4096.
Notes: Accessing 2 elements of array[] to bring them into cache, causes future accesses to these 2 elements

## Slide 18: Task 2: Using Cache as a Side Channel
1. FLUSH the entire array from the cache to make sure the array is not cached.
2. Invoke the victim function, which accesses one of the array elements based on the value of the secret. This action causes the corresponding array element to be cached.
3. RELOAD the entire array, and measure the time it takes to reload each element. Loading element corresponding to the secret element will be a cache hit, and be much faster.

## Slide 19: Listing 2: FlushReload.c
Since array[0] may be accidentally brought into cache before the attack, due to cache prefetching when some other program accesses variables in adjacent memory addresses smaller than &array[0], we use array[k*4096 + DELTA] for all k values, where DELTA is defined as a constant 1024

## Slide 20: Toy Example with DELTA=2
a[0*STEP] | a[0*STEP+1] | a[0*STEP+2] | a[0*STEP+3] | a[0*STEP+4] | a[0*STEP+5]
a[1*STEP] | a[1*STEP+1] | a[1*STEP+2] | a[1*STEP+3] | a[1*STEP+4] | a[1*STEP+5]
a[2*STEP] | a[2*STEP+1] | a[2*STEP+2] | a[2*STEP+3] | a[2*STEP+4] | a[2*STEP+5]
a[3*STEP] | a[3*STEP+1] | a[3*STEP+2] | a[3*STEP+3] | a[3*STEP+4] | a[3*STEP+5]
a[4*STEP] | a[4*STEP+1] | a[4*STEP+2] | a[4*STEP+3] | a[4*STEP+4] | a[4*STEP+5]
Reloaded Elements
Cache block accessed
by victim;
Fast reload by attacker
This part acts as a buffer to absorb any prefetching when accessing variables in adjacent memory addresses smaller than &a[0]

## Slide 21: Task 3: Place Secret Data in Kernel Space
Listing 3: MeltdownKernel.c
Line 1: saves the address of the secret data into the kernel message buffer ()
Use the secret once to bring it into cache
Line 3: create a data entry /proc/secret_data. When a user-level program reads from this entry, the read proc() function in the kernel module will be invoked, inside which, the secret variable will be loaded (Line 1) and thus be cached by the CPU

## Slide 22: Finding the Secret Data Address
After compilation, use the insmod command to install the kernel module, then use the dmesg command to find the secret data’s address from the kernel message buffer.
  In real Meltdown attacks, attackers have to figure out a way to get the address, or they have to guess.

## Slide 23: Task 4: Access Kernel Memory from User Space
This program will crash, since you are trying to access kernel memory from user space
Replace this address with the address obtained from Task 3

## Slide 24: Task 5: Handle Error/Exceptions in C
Instead of program crashing, we want to print out a message “"Memory access violation!”
To catch the exception SIGSEGV caused by accessing kernel memory address from user space, we emulate the try/catch clause in C++ using sigsetjmp() and siglongjmp(),

## Slide 25: Task 6: Out-of-Order Execution by CPU
Line 3 involves two operations at assembly code level:
  3.A assign content of kernel_adderess to kernel_data
  3.B check the data access permission, and if permission check fails, roll back any instructions (e.g., instruction 4) executed after the check)
Line 4: Load kernel_data into cache and then into CPU register
In-order execution: instructions 3.A, 3.B and 4 execute in order
Out-of-Order Execution: instruction 3.A executes first, then instructions 3.B and 4 execute in parallel in the CPU pipeline (since both 3.B and 4 depend on “kernel_data” loaded by 3.A)
3A
3B
4

## Slide 26: Meltdown Attack
Race condition between 3B and 4; either one may execute first
  If instruction 3B executes before 4, and permission check fails, then 4 will not execute at all
  If instruction 4 executes speculatively before 3B, and permission check fails, then roll back any effect of 4
The rolled-back instructions do not have any externally visible effect: variable “number” stays unchanged
However, “kernel_data”, the data stored at memory address “kernel_address”, has been brought into the cache (and CPU register), and attacker can find its value by cache side channel analyiss
Accessing kernel data (3A)
Permission check (3B)
Inst. that brings kernel data into cache (4)
They will be rolled back if permission check fails
Race condition

## Slide 27: MeltdownExperiment.c
Line 2: array[7 * 4096 + DELTA] will be loaded into the CPU cache due to Out-of-Order execution, but a memory access violation will occur subsequently, so its value will not be actually incremented at the end
Replace this address with the address obtained from Task 3

## Slide 28: Task 7: The Basic Meltdown Attack Task. 7.1: A Naive Approach
Instead of array[7 * 4096 + DELTA], we access array[kernel_data * 4096 + DELTA]
Using the FLUSH+RELOAD technique, we check the access time of array[i*4096 + DELTA] for i = 0, . . ., 255.
If we find out that only array[k*4096 + DELTA] is in the cache, we can infer that the value of the “kernel_data” is k.

## Slide 29: Task 7.2: Improve the Attack by Getting the Secret Data Cached
To maximize chance of success of attack, we can preload the kernel secret data into cache before launching the attack
The following user-level program uses system calls open() and pread() to access the secret data without leaking it to the user-level program by reading 0 bytes into a NULL buffer
  ssize_t pread(int fildes, void *buf, size_t nbyte, off_t offset);
Notes: ssize_t pread(int fildes, void *buf, size_t nbyte, off_t offset);

## Slide 30: Task 7.3: Using Assembly Code to Trigger Meltdown
To maximize chance of success, Meltdown_asm() runs a useless computation loop for 400 times, in order to occupy the ALUs to delay execution of Permission check, making it more likely to execute *after* instruction 4
“Useless computation” will cause delay to “Permission check” (3B), since they are both computation instructions; but not to (4), since (4) is a memory instruction, so they can execute concurrently
Accessing kernel data (3A)
Permission check (3B)
Inst. that brings kernel data into cache (4)
Useless Computation
Delays
Race condition

## Slide 31: Task 8: Make the Attack More Practical
The actual timing measurements may be noisy due to cache prefetching, OS scheduling, interrupts and other interference effects, making it difficult to set the proper value of CACHE_HIT_THRESHOLD that works always
Statistical technique: create a score array of size 256, one element for each possible secret value. We then run our attack for 1000 times. Each time, if our attack program says that k is the secret (this result may be false), we add 1 to scores[k]. After running the attack for many times, we use the value k with the highest score as our final estimation of the secret

## Slide 32: Statistical technique

## Slide 33
Spectre

## Slide 34: Non-Pipelined Instruction Execution (hypothetical)
2nd Instruction (Adrs: PC+2)
Fetch
Decode
Execute
1st Instruction (Adrs: PC)
Fetch
Decode
Execute
3rd Instruction (Adrs: PC+4)
Fetch
Decode
Execute
Time
One instruction completed every 3 cycles. Performance is much lower than pipelined execution.
Fetch
Decode
Execute
PC
PC - 2
PC - 4

## Slide 35: Pipelined Instruction Execution
Fetch
Decode
Execute
PC
PC - 2
PC - 4
2nd Instruction (Adrs: PC+2)
Fetch
Decode
Execute
1st Instruction (Adrs: PC)
Fetch
Decode
Execute
3rd Instruction (Adrs: PC+4)
Fetch
Decode
Execute
Time
Pipelining allows multiple instructions to be in progress simultaneously during any one processor clock cycle. While one instruction is fetched, another is decoded, and a third is executed.
Notes: Thumb instructions are 16 or 32 bits wide, with the majority being 16 bits. Thus, while the address held in PC is being used to read one 16-bit instruction from memory, the previous instruction (from address PC-2) is decoded, and the one before that (from address PC-4) is executed. One instruction completed every cycle.

## Slide 36: Out-of-Order Execution (or Speculative Execution)
Predict branch direction
Go Faster: Pipelining, branch prediction, & instruction speculation
add
load
branch
and
Speculate!
store
Speculate more!
Speculation correct: Commit architectural changes of and (register) & store (memory) instructions
Mis-speculate: Abort architectural changes (registers, memory); go in other branch direction

## Slide 37: Spectre Lab Tasks
Tasks 1 and 2: Side Channel Attacks via CPU Caches (same as Meltdown attack and can be omitted)
  Task 1: Reading from Cache versus from Memory
  Task 2: Using Cache as a Side Channel
Task 3: Out-of-Order Execution and Branch Prediction
Task 4: The Spectre Attack
Task 5: Improve the Attack Accuracy
Task 6: Steal the Entire Secret String

## Slide 38: Task 3: Out-of-Order Execution and Branch Prediction
In-order execution: Line 3 (data = data + 5) is executed only if condition (x < size) is true
Out-of-order execution: Line 3 may be executed speculatively before condition (x < size) is checked; its effects will be rolled back if (x < size) is false
  Condition check may be slow if x is in memory (not in cache)
  The CPU branch predictor predicts direction of each branch, and the predicted branch is executed speculatively before condition is checked
  If branch prediction is wrong, the speculative execution is rolled back, and the correct branch will be executed
data = 0;
check (if x < size)
data = data +5
Race condition if branch predictor
predicts condition to be true

## Slide 39: Listing 3: SpectreExperiment.c
The for loop starting from Line 3 invokes victim() with a small argument (from 0 to 9). These values are less than the value size, so the true-branch of the if-condition in Line 1 is always taken. This is the training phase, which essentially trains the branch predictor to expect the if-condition to be “true”.
We pass a larger value (97) to the victim() function (Line 5). This value is larger than size, so Line 2 should not be executed; but the branch predictor makes the prediction of “true”, so Line 2 will be executed speculatively.
We flush the variable “size” from the cache, in order to make the check “if (x < size)” slow due to memory access, so program will execute the branch speculatively based on branch prediction

## Slide 40: Task 4: The Spectre Attack
True-branch will never be executed if x is larger than the buffer size,
But at microarchitectural level, it can be executed speculatively and some traces can be left behind when the execution is rolled back

## Slide 41: Comparison w/ Stack Overflow Attack
(a) Situation when main program is running
(b) After procedure A() called
(c) Buffer overflow alters the return address from A().
  Can be garbage that causes program crash, or can be address of a malicious program
Checking array bounds (if (x < buffer_size)) prevents buffer overflow attack that writes to unauthorized addresses, but not Spectre attack that reads from unauthorized addresses through cache side channel

## Slide 42: Listing 4: SpectreAttack.c
Line 4 calculates the offset of the secret from the beginning of the buffer(if offset is unknown, must find it with testing or guessing)
The offset larger_x is larger than 10, and buffer[larger_x] contains value of the secret.
“return buffer[x]” in restrictedAccess(), and Lines 2, 3 in spectreAttack() will be executed speculatively to assign s= buffer[larger_x], and bring it into the cache. Its effects will be rolled back later, and the correct branch “return 0” will be executed to assign s=0, but value of buffer[larger x] is left in the cache, and attacker can find it with cache side channel
The code only steals the first byte of the secret.

## Slide 43: Task 5: Improve the Attack Accuracy
Statistical technique: create a score array of size 256, one element for each possible secret value. We then run our attack for 1000 times. Each time, if our attack program says that k is the secret (this result may be false), we add 1 to scores[k]. After running the attack for many times, we use the value k with the highest score as our final estimation of the secret
“You may observe that when running the code above, the one with the highest score is always scores[0]. Please figure out the reason, and fix the code above, so the actual secret value (which is not zero) will be printed out.”
  “return 0” in restrictedAccess() is always executed eventually, when the condition “if(x<buffer_size)” is checked to be false
  “return buffer[larger_x]” in restrictedAccess() may or may not be executed speculatively, depending on the race condition between it and the condition check
  So reloadSideChannel() is likely to see two cache hits, for values of 0 and buffer[larger_x]
  If we know that buffer[larger_x] ≠ 0, then we can simply ignore the value of 0.
  But what if buffer[larger_x] ==0? Then we cannot identify buffer[larger_x]

## Slide 44: Task 6: Steal the Entire Secret String
char *secret = "Some Secret Value";
  secret is a pointer to the memory address of the 0th array element secret[0] (‘S’)
  secret+1 is a pointer to the memory address of the 1st array element secret[1] (‘o’)
  …

## Slide 45: Meltdown vs. Spectre
Meltdown: an instruction accessing kernel memory causes an exception, but subsequent instructions are executed speculatively, and bring array[x*STEP] into cache
The speculative execution is rolled back upon the exception, but cache state is altered
Spectre: a branch condition should prevent execution of certain instructions, but subsequent instructions in the wrong branch are executed speculatively, and bring array[x*STEP] into cache
The speculative execution is rolled back upon getting the actual branch condition, but cache state is altered
(Assume each instruction is 16 bits (2 Bytes), hence the next instruction is n+2)