## Slide 1: On the Implications of the Meltdown & Spectre Design Flaws ISCA 2018 Panel
Mark D. Hill, Wisconsin, CCC, Google Sabbatical
Paul Kocher, Independent
Ruby B. Lee, Princeton & Teleputers
Simha Sethumadhavan, Columbia & Chip Scan
Timothy Sherwood, UCSB & Tortuga Logic

## Slide 2: Meltdown & Spectre Announced, January 2018 Photo from Ernst & Young Bldg (across the street)

## Slide 3: Panel Info (Hidden Slide)
Panel On the Implications of the Meltdown & Spectre Design Flaws
Computer Architecture 1.0 specifies the timing-independent functional behavior of a computer, while Micro-Architecture is the implementation techniques that improve performance. What if a computer that is completely correct by Architecture 1.0 can be made to leak protected information via timing, a.k.a., Micro-Architecture? This is done by the Meltdown and Spectre design flaws that were broadly revealed in January 2018. Meltdown leaks kernel memory, but software & hardware fixes exist. Spectre leaks memory outside of sandboxes and bounds checks, and it is scary.
This panel will explore implications of Meltdown and Spectre, especially that the definition of Architecture 1.0 is inadequate to protect information.
Going forward, is it time for Architecture 2.0 and, if so, what is it? If not, do we go forward with micro-architecture best practices and, if so, what are they?
Moderator
Mark D. Hill, University of Wisconsin-Madison
Panelists
Paul Kocher, Independent
Ruby B. Lee, Princeton University
Simha Sethumadhavan, Columbia University and Chip Scan Inc.
Timothy Sherwood, UC Santa Barbara and Tortuga Logic
When 12:00pm on Monday June 4, 2018

## Slide 4: The Set Up
Architecture 0.0: Each computer implementation was new, requiring all software to be rewritten (in machine/assembly language)
Architecture 1.0: the timing-independent functional behavior of a computer Micro-architecture: the implementation techniques to improve performance
Covert timing channels … one process to signal ... another … by modulating its own use of system resources [to be] observed by the 2nd process.
--1983/85 DoD “Orange Book”
ENIAC, etc. mid-20th Century
IBM 360 ISA, 1964

## Slide 5: The Problem & Opportunity
Question: What if a computer that is completely correct by Architecture 1.0 can be made to leak protected information via timing, a.k.a., Micro-Architecture?
Meltdown leaks kernel memory, but software & hardware fixes exist
Spectre leaks memory outside of bounds checks or sandboxes, and is scary
Implication: The definition of Architecture 1.0 is inadequate to protect information
Abandon speculation (for accelerators)? Not completely IMHO
Address in micro-architecture? Manage, not fix, like crime
Define Architecture 2.0? Whatever that is

## Slide 6: On the Implications of the Meltdown & Spectre Design Flaws ISCA 2018 Panel
Mark D. Hill, Wisconsin, CCC, Google Sabbatical
Paul Kocher, Independent
Ruby B. Lee, Princeton
Simha Sethumadhavan, Columbia & Chip Scan
Timothy Sherwood, UCSB & Tortuga Logic

## Slide 7: Spectre & Its Root Causes
Paul Kocher (paul@paulkocher.com)
ISCA
June 4, 2018
If the surgery proves unnecessary, we’ll revert your architectural state at no charge.
All trademarks are the property of their respective owners. This presentation is provided without any guarantee or warranty whatsoever.

## Slide 8: Addicted to speed
Performance goal
  Lowest time to reach the result same as running program in-order
Single-thread speed gains require getting more done per clock cycle
  Memory latency is slow and not improving much
  Clock rates are maxed out: Pentium 4 reached 3.8 GHz in 2004
How to do more per clock?
  Reducing memory delays  Caches
  Working during delays  Speculative execution
Public domain image of Pentium 4 die by Ritzchens Fritz

## Slide 9: Memory caches for dummies
Caches hold local (fast) copy of recently-accessed 64-byte chunks of memory
MAIN MEMORY
Big, slow
e.g. 16GB SDRAM
Set | Addr | Cached Data ~64B
0 | F0016280 31C6F4C0 339DD740 614F8480 | B5 F5 80 21 E3 2C.. 9A DA 59 11 48 F2.. C7 D7 A0 86 67 18.. 17 4C 59 B8 58 A7..
1 | 71685100 132A4880 2A1C0700 C017E9C0 | 27 BD 5D 2E 84 29.. 30 B2 8F 27 05 9C.. 9E C3 DA EE B7 D9.. D1 76 16 54 51 5B..
2 | 311956C0 002D47C0 91507E80 55194040 | 0A 55 47 82 86 4E.. C4 15 4D 78 B5 C4.. 60 D0 2C DD 78 14.. DF 66 E9 D0 11 43..
3 | 9B27F8C0 8E771100 A001FB40 317178C0 | 84 A0 7F C7 4E BC.. 3B 0B 20 0C DB 58.. 29 D9 F5 6A 72 50.. 35 82 CB 91 78 8B..
4 | 6618E980 BA0CDB40 89E92C00 090F9C40 | 35 11 4A E0 2E F1.. B0 FC 5A 20 D0 7F.. 1C 50 A4 F8 EB 6F.. BB 71 ED 16 07 1F..
Addr: 2A1C0700
Data: 9E C3 DA EE B7 D3..
Addr: 132E1340
Address:
132E1340
Data: AC 99 17 8F 44 09..
Addr: 132E1340
Data: AC 99 17 8F 44 09..
Fast
Slow
Fast
h(addr) to map to cache set
132E1340
Evict to make room
AC 99 17 8F 44 09..
MEMORY
CACHE
2A1C0700
Data:
AC 99 17 8F 44 09..
CPU
Sends address, Receives data
Reads change system state:
Next read to newly-cached location is faster
Next read to evicted location is slower

## Slide 10: Speculative execution
Violates software security requirement that the CPUs runs instructions correctly.
  if (uncached_value_usually_1 == 1)
  foo()
Instead of idling, CPUs can guess likely program path and do speculative execution
  Example:
  Branch predictor: if() will probably be ‘true’ (based on prior history)
  CPU starts foo() speculatively -- but doesn’t commit changes
  When value arrives from memory, if() can be evaluated definitively -- check if guess was correct:
    Correct: Commit speculative work – performance gain
    Incorrect: Discard speculative work
Regular execution
Erroneous speculative execution
Set up the conditions so the processor will make a desired mistake
Mistake leaks sensitive data into a covert channel (e.g. state of the cache)
Fetch the sensitive data from the covert channel

## Slide 11: Conditional branch (Variant 1) attack
if (x < array1_size)
y = array2[array1[x]*4096];
Assume code in kernel API, where unsigned int x comes from untrusted caller
Execution without speculation is safe
  CPU will not evaluate array2[array1[x]*4096] unless x < array1_size
What about with speculative execution?

## Slide 12: Conditional branch (Variant 1) attack
Before attack:
  Train branch predictor to expect if() is true (e.g. call with x < array1_size)
  Evict array1_size and array2[] from cache
if (x < array1_size)
y = array2[array1[x]*4096];
Contents don’t matter
Memory & Cache Status
array1_size = 00000008
Memory at array1 base address:
8 bytes of data (value doesn’t matter) [… lots of memory up to array1 base+N…]
09 F1 98 CC 90...(something secret)
array2[ 0*4096]
array2[ 1*4096]
array2[ 2*4096]
array2[ 3*4096]
array2[ 4*4096]
array2[ 5*4096]
array2[ 6*4096]
array2[ 7*4096]
array2[ 8*4096]
array2[ 9*4096]
array2[10*4096]
array2[11*4096]
Uncached
Cached
  
only care about cache status

## Slide 13: Conditional branch (Variant 1) attack
Attacker calls victim with x=N (where N > 8)
  Speculative exec while waiting for array1_size
    Predict that if() is true
    Read address (array1 base + x) w/ out-of-bounds x
    Read returns secret byte = 09 (fast – in cache)
    Request memory at (array2 base + 09*4096)
    Brings array2[09*4096] into the cache
    Realize if() is false: discard speculative work
  Finish operation & return to caller
Attacker measures read time for array2[i*4096]
  Read for i=09 is fast (cached), revealing secret byte
  Repeat with many x (eg ~10KB/s)
if (x < array1_size)
y = array2[array1[x]*4096];
Memory & Cache Status
array1_size = 00000008
Memory at array1 base address:
8 bytes of data (value doesn’t matter) [… lots of memory up to array1 base+N…]
09 F1 98 CC 90...(something secret)
array2[ 0*4096]
array2[ 1*4096]
array2[ 2*4096]
array2[ 3*4096]
array2[ 4*4096]
array2[ 5*4096]
array2[ 6*4096]
array2[ 7*4096]
array2[ 8*4096]
array2[ 9*4096]
array2[10*4096]
array2[11*4096]
Uncached
Cached
  
Contents don’t matter
only care about cache status

## Slide 14: Indirect branches (Variant 2)
Can go anywhere instantly (“jmp [rax]”)
  Poison predictor so victim speculative executes a ‘gadget’ that leaks memory
Attack steps
    Poison branch predictor/BTB so speculative execution will go to gadget
    Evict from the cache or do other setup to encourage speculative execution
    Execute victim so it runs gadget speculatively
    Read sensitive data from covert channel
    Repeat
Is x < y
no
yes
Jump to address x
Conditional branch
Indirect branch

## Slide 15
Variations
Attack scenarios
  user process attacks kernel/driver
  user process attacks user
  intra-process sandbox escape (JavaScript, safe languages…)
  user process attacks special modes (SGX/TrustZone/SMM…)
  hypervisor guests attack each other/host
  remote timing attack
  …
Speculation scenarios
  conditional branch
  indirect jump
  return instruction (e.g. Skylake w/ return stack buffer empty)
  speculative store bypass
  data speculation
  …
Covert channels
  Changes in cache state [many variations]
  Cache state on entry affects timing of later operations that use shared resources
  Other digital (FPU, buffers…)
  Analog (power, RF…)
  …
Target CPUs
  ARM
  Intel
  AMD
  Power
  Sparc
  …
Many flavors

## Slide 16
LFENCE
CPU
Variant 1 Mitigation: Speculation-barrier instruction (e.g. LFENCE)
  Idea: Software developers insert barrier on all vulnerable code paths in software
  Efficient: No performance impact on benchmarks or other legacy software
  Simple & effective
App image: CC0 Creative Commons, Free for commercial use , No attribution required
https://pixabay.com/en/app-software-contour-settings-1013616/
Abstraction boundaries
  Insert LFENCEs manually?
  Often millions of control flow paths
  Too confusing - speculation runs 188++ instructions, crosses modules
  Too risky – miss one and attacker can read entire process memory
  Put LFENCES everywhere?
  Abysmal performance - LFENCE is very slow (+ no tools)
  Not in binary libraries, compiler-created code patterns
  Insert by smart compiler?
Transfers blame after breach to SW: “you should have put an LFENCE there”
Software
operating systems
drivers
web servers
interpreters/JITs
databases
:
CPU architecture
Machine language
Compiler
Higher-level language
  Protect all potentially-exploitable patterns = too slow
    Compilers judged by performance, not security
  Protect only known-bad bad patterns = unsafe
    Microsoft Visual C/C++ /Qspectre unsafe for 13 of 15 tests
    https://www.paulkocher.com/doc/MicrosoftCompilerSpectreMitigation.html
(for CPU developer)… and Variant 2 also messy or no fix
?
“All of this is pure garbage”
-- Linus Torvolds
https://lkml.org/lkml/2018/1/21/192

## Slide 17: Risk in context
Spectre doesn’t change the magnitude of the risk, but adds to the mess
      Poor mitigation options (fixes -> new risks)
      Psychology of unfixed vulnerabilities
Because of software bugs, computer security was in a dire situation

## Slide 18: Is Spectre a bug?
Everything works according to the textbook
  Branch predictor is learning from history, as expected
  Speculative execution unwinds architectural state correctly
  Reads are fetching data the victim is allowed to read (unlike Meltdown)
  Caches are allowed to hold state
  Covert channels known to exist (+ very hard to eliminate)
No violation of architecture specs
?!

## Slide 19: Architecture  Software security gap
CPU architectures are under-specified
    Confidentiality (cache behavior, predictors, debug modes, power consumption, RF, internal sensors/PLLs…)
    Integrity (traditional fault/glitch attacks, RowHammer, clkscrew, supply chain attacks…)
    Availability (when can SW degrade performance? crash the system? destroy the CPU?…)
    Difficult to specify… and must actually achieve (with high probability)
Software developers forced to rely on microarchitectural guesses
    Often wrong today (-> CacheBleed…)
    Future chips may be completely different
CPU architectures rely on false assumptions
    Assumes SW is perfect -> failure to improve bug survivability (e.g. CFI, CHERI…)
    Assumes HW is perfect -> HW security is doomed by excessive complexity
    Assumes no trade-offs between security & performance -> can’t maximize both
    Assumes architectural ambiguity is OK -> ambiguity is a security problem (not a benign optimization opportunity)

## Slide 20
Past: Performance dominated the economics of technology
Today: Costs of insecurity > Value of performance gains
Leadership challenge
Today’s leaders developed during 50+ years where performance > security
Technical challenges
Architecting & implementing robust and resilient systems
$1012-$1013 year1
Magnitude: $1011/year2
1 “Estimating the Global Cost of Cyber Risk” (https://www.rand.org/pubs/research_reports/RR2299.html): $275B-$6.6T direct costs depending on assumptions, and $799B-$22.5T incl. indirect costs.
2 My estimate. For reference, Intel’s entire 2017 revenues were $62.8B, ARM <$2B.

## Slide 21: Spectre is a symptom
Today it’s crazy to use the same HW+OS for everything
  video games + medical + email + wire transfers
Need faster + safer flavors
  ‘Safer’ = less complex (not just a different mode like TrustZone, Intel SGX)
  Accept some inefficiency (performance, die area, power, developer time…)
Faster & safer can co-exist
  Common for performance/power: ARM’s big.LITTLE architecture, GPU, TPU
  Security examples: Pay TV smart cards, Rambus CryptoManager cores, Apple Enclave…

## Slide 22
Thank you!
paul@paulkocher.com

## Slide 23
Extra slides

## Slide 24: Exponential changes
Attacker perspective:
Complexity  Bugs
Devices  Targets
Economic activity  $

## Slide 25
Abstraction creates security challenges
Dependencies & assumptions
Security goals
Security-critical details hidden in layers
Needs of distant layers unclear
People specialize then miss big picture
Economics don’t fund adequate investment
Risks in other layers deter improvements
Changes aren’t communicated across layers
Exponential growth
Microarchitectures
Clouds
CPU architectures
Foundations
People
Business objectives
Society
Nation states
Logic block
Abstractions
Operating systems
Languages
Compilers
Protocols
Libraries/frameworks
Applications
Browsers
Chip
Circuit board
Drivers
U.I.
Transistors
AI

## Slide 26: Mitigations: Indirect branch variant
Intel/AMD (x86):
    New MSRs created via microcode
        Low-level control over branch target buffer (O/S only)
        Performance impact – limited use
    Retpoline proposal from Google
        Messy hack -- replace indirect jumps with construction that resists indirect branch poisoning on Haswell
        Microcode updates to make retpoline safe on Skylake & beyond
ARM: No generic mitigation option
      Fast ARM CPUs broadly impacted, e.g. Cortex-A9, A15, A17, A57, A72, A73, A75...
      Often no mitigation, but on some chips software may be able to invalidate/disable branch predictor (with “non-trivial performance impact”)
          See: https://developer.arm.com/support/security-update/download-the-whitepaper
Mitigations are messy (for all Spectre variants + Meltdown)
      Software must deal with microarchitectural complexity
      Mitigations for all variants are really hard to test
“All of this is pure garbage”
-- Linus Torvolds
https://lkml.org/lkml/2018/1/21/192

## Slide 27: ISCA Panel: Architecture 2.0
Ruby B. Lee
Princeton University

## Slide 28
Architects need to understand the bigger picture
What are the Fundamental Hardware issues behind Spectre/Meltdown attacks?

## Slide 29: Architecture 2.0 Design Approaches
Complete Clean Slate Design - Change everything: programming paradigm, ISA, microarchitecture, etc.
Rethink microarchitecture performance optimization
    Optimization through randomization?
Define Design Principles for Security, e.g.,
    Access to a different security domain MUST first be checked
    Give the attacker NO information

## Slide 30: Architecture 2.0
Design Security-Aware Computer Architecture
      Yes, Yes, YES!
      Grand challenge for architecture creativity:
      Rethink performance and security optimization!
      through randomization?

## Slide 31: We can solve this!
Simha Sethumadhavan
simha@columbia.edu
Simha Sethumadhavan

## Slide 32: But first, recognize (again) that is a serious problem
Hardware is the root of security and trust. HW compromises will result in catastrophic failures.
Quote from Google Chrome Security Engineering team (May 28th 2018)
Simha Sethumadhavan

## Slide 33: We have known about this problem (& solns) for 30+ years
Timing and storage channels occur when two or more processes share a resource in space and/or time. Resource can be any microarchitectural structure: caches, predictors, pipelines, energy mgmt. etc.
Three solution categories
  Constant time: Make everything take the same amount of time at microarch level. For instance, add latency = worst case load latency in the system (page fault?). anti comp arch.
  Partitioning in time and space: Don’t share and cleanup state after use. High cost due throughput loss (no sharing) and a large number of cold misses (cleanup). anti comp arch.
  Randomization: Slow down the attacker. Two types: randomizing time, or randomizing access to shared structures. Low perf overhead but not preferred by security puritans
Simha Sethumadhavan

## Slide 34: There is a fourth option that is easy and feasible.
Basic Idea
Punish the attacker not the victim.
Randomization can be secure enough in many contexts.
Simha Sethumadhavan

## Slide 35: There is a fourth option that is easy and feasible.
Consider a machine with these three options:
High security but high cost: static partitioning and/or constant time
Low cost but reasonable security: randomization
No cost and no security: normal high performance mode
Determine threat using a predictor (basically an anomaly detector with one sided error) to determine threat level.
Move to safe mode when threat is detected or in randomization mode, switch to high security (or change application keys) when entropy runs out.
We know how to do this. And, this can happen completely without user involvement or programmer support.
Simha Sethumadhavan

## Slide 36: Only people in this room can solve this problem
Baby steps
  Think about including a security evaluation section in your paper
  Pick a less leaky option if you are designing hardware
  Say something about security in each computer architecture lecture
The world is really flat (and not in a good way) because of HW 0-days.
Please help stop this.
Simha Sethumadhavan

## Slide 37: Timothy Sherwood

## Slide 38
Deterministic Attack
Javascript Interpreter
Browser Process
OS Memory Layout
  No user level access to pagemap
  Deduplication
  Memory pressure manager
  Address Space Randomization
Cache Hierarchy
  No explicit cache flush
  All the stuff we know and love
DRAM Controller, etc.
“hard” to exploit is not good enough
a tale from Rowhammer
2 weeks.
how long?

## Slide 39
Application
Operating System
Architecture
new verifiable abstractions
respect the adversary
timing is explicit in hw